## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
30
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28/04/21 – 05/05/21
Introduction to OpenSees
Introduction to STKO – Scientific Toolkit for OpenSees
Model definition overview
Geometry, Interactions, Selection sets, Local axes
Physical properties
June-October (once a week)*
Element properties
Definitions and Conditions - Next webinar 07/07/2021
Mesh and Analysis (2 hours on the Analysis Commands)
Postprocessing and results visualization
Modal and response spectrum analysis
Linear, nonlinear static and dynamic analysis
Reinforced concrete and masonry frame structures
(+ softening and mesh objectivity, diaphragms modelling, joints modeling, infill panels…)
*Only one in August
1
2
6
11
12
20
Full syllabus available here
THEORY
PRACTICE
INTRO
3
4
5

## Slide 3
GET STARTED in OpenSees with STKO
Element
properties
6
displBeamColumn
definition
creation
assignment
forceBeamColumn
Comparison and use
30 June 2021
Element properties
6
3D frame structures

## Slide 4
Page 4
Element prop.
Definition
Element properties are namely the finite element formulation of the model. The element properties are the related to the FE method used and the way the solution is going to be identified in our model. In OpenSees you have many finite element formulations not only one as in many commercial FEM.
You are practically telling to your geometry how
it should behave in the analysis.
The choice of elements depends on the material,
the dimension of the element and the type of discretization/mesh desidered,
and of course on the type of result we wish to obtain.
Ex. displacement based elements for pile-soil interaction - discretization
force based elements for 3D frame structures - localization

## Slide 5
Page 5
Element prop.
OpenSees and STKO
construct objects
Modelbuilder
See support file: ex8.tcl, ex8.scd
create and assign physical properties
STKO
Integration scheme specified in the special purpose physical property object BeamSectionProperty
+
Notes: Missing last element screeshot

## Slide 6
element dispBeamColumn $eleTag $iNode $jNode $numIntgrPts $secTag $transfTag
<-mass $massDens> <-cMass> <-integration $intType>
Page 6
Element prop.
X-Objects
all elements in OpenSees correspond to Element Property X-Objects written in Python for STKO
$eleTag
<cMass>
$iNode
OpenSees Commands parameters are X-Objects attributes in STKO. Each attribute has specific metadata, of a specific type
(integer, real, string, vector etc.)
See PyMpc classes MpcXObject, MpcAttribute, MpcAttributeMetadata
$transfType
<-mass>
$jNode

## Slide 7
Page 7
Creation and assignments
Element prop.
available operations
color coding
All geometries with an assigned physical properties need to have an assigned element properties too, and vice versa.
TIP: Select all elements with a specific physical property assigned to assign the element properties.
TIP: How to read results on beamColumn elements???
reaction.force = results at the nodes (linear along the element)
    section.force = results at the gauss points
    localForce = results in the extremities of the elements
    (also different at the two sides)
Not Used Referenced Used
Used
Referenced
Drag on selection
Drag on selection + Ctrl

## Slide 8
Page 8
Element prop.
displBeamColumn vs
“displacement is the unknown variable, the element computes the strain from the displacement, gives them to the section that provides stress results”
The deformation is considered continuous along the element
See OpenSees Manual
and prof. Scott blog post on «A tale of two element formulations»
»
forceBeamColumn
“assumes the distribution of forces along the elements and then computes the deformations with an iterative process”
The force is considered continuous, and deformation is found iteratively. Displacement can be discontinuous here.
    This is true for all displacement based and force based FE in general

## Slide 9
Page 9
Comparison
Softening and mesh objectivity
strain-softening in constitutive models - non-uniqueness of the solution
(elements do not behave all the same in the presence of cracks, the solutions depends on the element size or integration size)
displacement field becomes discontinuous
(displacement jumps, not good for standard FEM! as we assume the solution to be derivable)
however we still want to use stress-strain models
strain localizes into a narrow band of elements, the energy dissipation depends on the element characteristic length
displacement-based and force-based elements behave differently
(he characteristic length depends on the size of finite element for displacement based, but if you have higher order integration schemes or force based elements, then it is related to the integration scheme. Therefore the solution depends on the mesh or the integration type and this is something that should never happen)

## Slide 10
Page 10
Comparison
Softening and mesh objectivity
    1 Force-based – 5 gp
    1 Force-based – 10 gp
    1 Disp-based – 5 gp
    1 Disp-based – 10 gp
    5 Disp-based – 5 gp
fixed
Fz = -300 kN
Ux = 200 mm
Cantilever columns, concentrated loads on the end.
See support file: ex9.scd

## Slide 11
Page 11
Comparison
Softening and mesh objectivity
    strain localization in the forceBeamColumn (continuous moment assumption not a continuous curvature as in displacement based)
    with more integration points the forceBeamColumn dissipates much less energy, and there is a difference in the post peak response
    changing the number of integration point in displacement based element does not change anything
    the discretization instead has an effect

## Slide 12
Page 12
Comparison
Fracture energy regularization
See support file: utils_06.xls
fracture energy
regularized fracture energy
scaling
factor
(reference length)
(characteristic length)

## Slide 13
Page 13
Comparison
Softening and mesh objectivity
    closer responses after regularization, not perfectly overlapping but closer (constant state of deformation assumption not real, there is bending)
    displacement based response can come closer to the force based if discretized
    the regularization affects only the dissipated energy, not the strain
See support file: ex10.scd

## Slide 14
Page 14
Use
Shear response
fiber-section only deals with P-My-Mz components (Euler-Bernoulli)
you can include shear deformability (Timoshenko) with sectionAggregator
shear forces at the element level are always present for equilibrium
shear forces at the section level are present only if included with sectionAggregator
shear stress-strain law should be regularized as usual
displacement-based elements do not support shear deformation (simple Euler-Bernoulli formulation)
use forceBeamColumn elements for shear

## Slide 15
Page 15
Use
Shear response
See support file: ex11.scd & ex12.scd

## Slide 16
Page 16
Comparison
OpenSees implementation – element loads
    Again, the displBeamColumn assumes continuous displacement along the element and then computes the forces.
    The forceBeamColumn assumes the forces continuous along the element and then iteratively finds the deformation.
force-based
displacement
based
See support file: ex13.scd
element load
discretization
    This is true only for OpenSees

## Slide 17
Page 17
Element prop.
displBeamColumn vs
“displacement is the unknown variable, the element computes the strain from the displacement, gives them to the section that provides stress results”
forceBeamColumn
“assumes the distribution of stresses along the elements and then computes the strain with an iterative process”
Requires a fine mesh for non-linear problems
Characteristic length = element
Only Euler-Bernoulli no shear
Element loads do not affect directly the section response
One element per member is enough if you are studying material nonlinearities
Characteristic length = gauss point
Shear considered in sectionAggregator
Element loads affect directly the section response

## Slide 18
Page 18
Assignment
Assignment
Apply the comparisons operated in today’s class to the frame structure of last week.
See support file: ex8.tcl, ex8.scd

## Slide 19
Page 19
Element prop.
Other elements we will encounter…
zeroLengthElement
HingedBeam
MasonryInfillWallElement
truss
ASDShellQ4
See support file: ex14.tcl
concentrated plasticity
infill walls
Shear walls

## Slide 20
Page 20
RESOURCES & REFERENCES
R&R
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Nonlinear finite element formulations
        A tale of two element formulations
        Numerical integration options
        Massimo’s OpenSees support group
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos

## Slide 21: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick