## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
30
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28/04/21 – 27/10/2021
Introduction to OpenSees
Introduction to STKO – Scientific Toolkit for OS
Model definition overview
Geometry, Interactions, Selection sets, Local axes
Physical properties
Element properties
Definitions and Conditions
Mesh and Analysis
Analyses Command (part 1-2)
Analyses Command (part 3-4)
Postprocessing and results visualization
Linear elastic analysis
Material and geometrical nonlinearities
Modelling approaches to plasticity
Nonlinear static (pushover) analysis
Modal and response spectrum analysis
Nonlinear static and dynamic analysis
Reinforced concrete and masonry frame structures
(+ softening and mesh objectivity, diaphragms modelling, joints modeling, infill panels…)
15
20
Full syllabus available here
THEORY
PRACTICE
INTRO
1
2
3
4
5
6
7
8
9
10
11
12
13
14

## Slide 3
GET STARTED in OpenSees with STKO
Nonlinear
static
analysis
Pushover
Sensitivity analysis
Lateral load distribution patterns
22 September 2021
Nonlinear static (pushover) analysis
Load Control vs Displacement control
15
15

## Slide 4
Page 4
Pushover
Example
7 constrained nodes for pushover load pattern application
3D frame structure with rigid diaphragms

## Slide 5
Softening
Page 5
Pushover
PUSHOVER
Load control vs Displacement Control
The user defines how the loads are incremented over time.
The integrator defines how the loads are incremented over time.
Apply an sp = maximum displacement expected
Set duration = timeSeries duration
Read (-) sum of reaction at the base as maximum load capacity reached
Not for a force profile application !!!
Apply a lateral load = 1
(if with Penalty choose the order of magnitude close to the expected value to avoid numerical errors)
Set target displacement = maximum displacement expected
Read load multiplier as maximum load capacity reached

## Slide 6
Page 6
Pushover
Constant and triangular lateral force distribution
See ex22.scd

## Slide 7
Page 7
NL Materials
Modal proportional lateral load distribution
MODE 1
Translation in the
–X direction
Each constrained node is pushed of a force proportional to the eigenvector of the principal mode of the structure.
See ex23.scd

## Slide 8
Page 8
NL Materials
Modal proportional lateral load distribution
See ex23.scd

## Slide 9
Page 9
NL Materials
Mass proportional lateral load distribution
Each constrained node is pushed of a force proportional to the eigenvector of the principal mode of the structure.
See ex24.scd

## Slide 10
Page 10
NL Materials
Mass proportional lateral load distribution
See ex24.scd

## Slide 11
Page 11
Pushover
Results extraction
TRIANGULAR
MODAL PROPORTIONAL
MASS PROPORTIONAL*
*comparison with the other load patterns is not as relevant here as a different mass distribution was applied here to vary the results

## Slide 12
Page 12
Pushover
Comparison

## Slide 13
Page 13
MORE RESOURCES & REFERENCES
R&R
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Geometric nonlinearities in OpenSees
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos

## Slide 14: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick