## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
40!
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28/04/21 – 05/05/21
Introduction to OpenSees
Introduction to STKO – Scientific Toolkit for OpenSees
Model definition overview
June-October (once a week)*
Geometry, Interactions, Selection sets, Local axes Physical properties - Next webinar 23/06/2021
Element properties
Definitions and Conditions
Mesh and Analysis (2 hours on the Analysis Commands)
Postprocessing and results visualization
Modal and response spectrum analysis
Linear, nonlinear static and dynamic analysis
Reinforced concrete and masonry frame structures
(+ softening and mesh objectivity, diaphragms modelling, joints modeling, infill panels…)
*Only one in August
1
2
4
11
12
20
Full syllabus available here
THEORY
PRACTICE
INTRO
3

## Slide 3
GET STARTED in OpenSees with STKO
Geometry
Interactions
Selection sets
Local axes
3
Interactions
creation
update
use
Geometry
Selection
sets
Local
axes
definition
types
implementation
geomTransf
default assignment in STKO
modifications
OpenSees and STKO
Brep vs Orphan mesh
Work Tree and commands in STKO
16 June 2021
Geometries, interactions, selection sets, local axes
3
+ 2 python utilities

## Slide 4
GET STARTED in OpenSees with STKO
Geometry
Interactions
Selection sets
Local axes
3
Interactions
creation
update
use
CAD in STKO
Brep vs Orphan Mesh
16 June 2021
Geometries, interactions,
selection sets, local axes
3
Geometry and Mesh
OpenSees
Query
Geometry
Selection
sets
Local
axes
definition
types
implementation
geomTransf
default assignment in STKO
modifications

## Slide 5
Page 5
Geometry
Geometry in OpenSees
construct objects
Modelbuilder
See support file: ex6.tcl, ex6.scd
draw objects
CAE

## Slide 6
Page 6
Geometry
Geometry in STKO
Orphan nodes and elements are components of a finite element mesh that exist without any associated geometry. The mesh information has been orphaned from its parent geometry.
Geometries are defined by their boundaries, the model is constituted by topological components (faces, edges and vertices) and the connection between them. Only at the end the geometry will be converted into mesh.
Orphan Mesh
Boundary representation BRep
A face is a bounded portion of a surface;
an edge is a bounded piece of a curve
and a vertex lies at a point.

## Slide 7
Page 7
Geometry
CAD Commands
Creates a compound of the selected geometries, a "composite" geometry made up of different items that preserve their own geometrical features.
Creates a unique geometrical entity from two or more curves.
Definitions
Creates a unique face from two or more faces of the starting objects.
Boolean operation. Merges the selected geometries.
Boolean operation. Unites the selected geometries.
Identifies the subclasses of the object by splitting it into its components.

## Slide 8
Page 8
Geometry
CAD Commands
Comparisons (2 solids)
12 vertices
20 edges
11 faces
2 solids
12 vertices
20 edges
10 faces
1 solid
16 vertices
24 edges
12 faces
2 solids

## Slide 9
Page 9
Geometry
CAD Commands
Comparisons (2 faces)
6 vertices
7 edges
2 faces
6 vertices
7 edges
2 faces
8 vertices
8 edges
2 faces
TIP: rename your geometry to speed up selection

## Slide 10
Page 10
Geometry
CAD Commands
Comparisons (2 polylines)
1 wire
8 vertices
8 edges
10 vertices
12 edges
8 vertices
8 edges
2 wires
4 vertices
4 edges
x

## Slide 11
Page 11
Geometry
Geometry and Mesh
The MESH reflects the GEOMETRY! Disjoint geometry? Disjoint mesh!!!
See Massimo’s Common Errors webinar:
https://www.youtube.com/watch?v=HsgcSR4jj4Q
disjoint geometries
Linked geometry (equalDOF)
joined geometries

## Slide 12
Page 12
Geometry
Query
joined geometries
disjoint geometries

## Slide 13
Page 13
Geometry
Python utility
See support file: utils_3.py
Create geometries from the Python API
See the PyMpc documentation: https://asdeasoft.net/stko-wiki/page5.html#sec18

## Slide 14
GET STARTED in OpenSees with STKO
Geometry
Interactions
Selection sets
Local axes
3
Interactions
creation
update
use
Types
Definition
16 June 2021
Geometries, interactions, selection sets, local axes
3
Implementation in STKO
Geometry
Selection
sets
Local
axes
OpenSees and STKO
Brep vs Orphan mesh
ork Tree and commands in STKO
geomTransf
default assignment in STKO
modifications

## Slide 15
Page 15
Interactions
Interactions
Connect geometries, elements that cannot be drawn, (for e.g. zerolength elements are collapsed geometries and cannot be drawn in the CAD environment of STKO).
In interactions you need to define
two types of nodes/elements :
Primary
Secondary
Definition
Interactions do not exist in OpenSees, they are a construct of STKO for:
Kinematic Constraints assignment
Retained masters
(in equations)
Constrained slaves
(displacement and rotations equal to the retained nodes)
Element assignments
Beginning of the element
End of the element
(giving the orientation of the element)

## Slide 16
Page 16
Interactions
Interactions
Types
Kinematic Constraints assignment
equalDOF (dispc = dispr)
rigidDiaphragm (dispc = dispr + rotr*dist)
rigidLink (same as rD for 2 nodes)
Element assignments
zeroLength
twoNodeLink
Contact Elements
TIP: At times, primary and secondary nodes are interchangable, others NO!!!! At time it has a physical meaning (kinematic constraints) or a compatibility problem with the chosen Constraint Handler.

## Slide 17
Page 17
Interactions
Interactions
Implementation
TIP: the type of interactions you define will be relevant in the appropriate choice
of CONSTRAINT HANDLER (don’t miss our classes on the AnalysisCommand )
Select retained geometries (masters)
Enter
Select constrained geometries (slaves)
Enter
Assign a multi-point constraint condition to the interaction
or
Assign an element to the interaction
Kinematic Constraints assignment
Element assignment

## Slide 18
GET STARTED in OpenSees with STKO
Geometry
Interactions
Selection sets
Local axes
3
Interactions
Definition, creation, update, use
16 June 2021
Geometries, interactions,
selection sets, local axes
3
Geometry
Selection
sets
Local
axes
OpenSees and STKO
Brep vs Orphan mesh
ork Tree and commands in STKO
definition
types
implementation
geomTransf
default assignment in STKO
modifications

## Slide 19
Page 19
Selection sets
Selection sets
Optional
Save time during selection, for assignment operations
Recreate interactions easily if they need to be erased
Hide/Show elements at a fast pace
Required
to set up a Monitor,
to use the Region Command,
to operate an analysis in Displacement control
Multipurpose tools in STKO, you can use them for numerous objectives.
Definition, creation, update, use

## Slide 20
GET STARTED in OpenSees with STKO
Geometry
Interactions
Selection sets
Local axes
3
Interactions
16 June 2021
Geometries, interactions,
selection sets, local axes
3
Geometry
Selection
sets
Local
axes
OpenSees and STKO
Brep vs Orphan mesh
ork Tree and commands in STKO
definition
types
implementation
creation
update
use
default assignments in STKO
geomTransf command
modifications
geomTransf
default assignment in STKO
modifications

## Slide 21
Page 21
Local axes
Local axes in OpenSees
node 1 0.0 0.0 0.0
node 2 10.0 0.0 10.0
x’
z’
y’
x’
z temp (on the xz plane not aligned with x)
vecXZ -5.0 0.0 -2.0
y’
x
y
z
z’
xz plane

## Slide 22
Page 22
Local axes
geomTransf command in OpenSees
The geometric-transformation command is used to construct a coordinate-transformation (CrdTransf) object, which transforms beam element stiffness and resisting force from the basic system to the global-coordinate system. The command has at least one argument, the transformation type (Linear, PDelta, Corotational).
TIP: For the standard OpenSees beam-column elements, the difference between geometric linear and geometric nonlinear analysis lies in the geometric transformation alone, since the elements have no internal geometric nonlinearity.

## Slide 23
Page 23
Local axes
geomTransf command in OpenSees
geomTransf Linear $transfTag $vecxzX $vecxzY $vecxzZ <-jntOffset $dXi $dYi $dZi $dXj $dYj $dZj>
$transfTag | transformation tag
$vecxzX $vecxzY $vecxzZ | X, Y, and Z components of vecxz, the vector used to define the local x-z plane of the local-coordinate system. The local y-axis is defined by taking the cross product of the vecxz vector and the x-axis. These components are specified in the global-coordinate system X,Y,Z and define a vector that is in a plane parallel to the x-z plane of the local-coordinate system.
$dXi $dYi $dZi | joint offset values -- offsets specified with respect to the global coordinate system for element-end node i
$dXj $dYj $dZj | joint offset values -- offsets specified with respect to the global coordinate system for element-end node j
i
j
end offset
section offset

## Slide 24
Page 24
Local axes
Default assignment in STKO
Direction of drawing defines default assignment of the characteristic axis
(x for an edge, z for a face)
i
j
j
i
1
2
3
4
To use the STKO default in your tcl script use in your geomTransf:
for edges (beams in the X-Y plane) use vecXZ = [0, 0, 1]
for edges (columns in the Y-Z or X-Z plane) use vecXZ = [1, 0, 0]

## Slide 25
Page 25
Local axes
Modify local axes in STKO
Use Reverse or Make Coherent to change the default local axes assignments.
If you move or explode your geometry, local axes modifications will be lost!!!

## Slide 26
Page 26
Local axes
Python utility
See support file: utils_4.py
Find the wrong oriented column
Selection sets

## Slide 27
Page 27
Local axes
See support file: utils_4.py
Find the wrong oriented column
Selection sets
Python utility

## Slide 28: «OpenSees does NOT have the concept of unit system»
See support file from WEEK 1: utils0.tcl
4
DAY
Since the last unit mistake on the forum
(I am counting my mistakes too!)

## Slide 29
Page 29
Unit System
Consistent Units |  |  |  | 
Length | m | mm | ft | in
Time | s | s | s | s
Mass | kg | ton | lbf × s2/ft | lbf × s2/in
Force | N | N | lbf | lbf
Temperature | C | C | F | F
Velocity | m/s | mm/s | ft/s | in/s
Acceleration | m/s2 | mm/s2 | ft/s2 | in/ s2
Angular velocity | rad/s | rad/s | rad/s | rad/s
Density | kg/m3 | ton/mm3 | slug/ft3 | lbf × s2/in4
Moment | N × m | N × mm | ft × lbf | in × lbf
Stress | Pa | Mpa | psf | Psi
Energy | J | mJ | ft × lbf | in × lbf
g-Gravity Constant | 9.81E+00 | 9.81E+03 | 3.22E+01 | 3.86E+02
Steel Density | 7.83E+03 | 7.83E-03 | 1.52E+01 | 7.33E-04
Steel Modulus | 2.07E+11 | 2.07E+05 | 4.32E+09 | 3.00E+07

## Slide 30
Page 30
MORE RESOURCES & REFERENCES
R&R
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos

## Slide 31: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick