## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
30
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28/04/21 – 05/05/21
Introduction to OpenSees
Introduction to STKO – Scientific Toolkit for OpenSees
Model definition overview
Geometry, Interactions, Selection sets, Local axes
Physical properties
Element properties
June-October (once a week)*
Definitions and Conditions
Mesh and Analysis - Next webinar 14/07/2021
Analysis Command (part 1-2-3-4)
Postprocessing and results visualization
Modal and response spectrum analysis
Linear, nonlinear static and dynamic analysis
Reinforced concrete and masonry frame structures
(+ softening and mesh objectivity, diaphragms modelling, joints modeling, infill panels…)
*Only one in August
1
2
7
11
12
20
Full syllabus available here
THEORY
PRACTICE
INTRO
3
4
5
6

## Slide 3
GET STARTED in OpenSees with STKO
Definitions
and Conditions
7
Definitions
07 July 2021
Definitions and Conditions
7
Conditions
Linear
Path
Path
timeSeries
Constraints
Loads
Masses
single-point
multi-point

## Slide 4
Page 4
OpenSees
Domain
SP_Constraint
Timeseries
MP_Constraint
LoadPattern
LOGIC AND ABSTRACTIONS
ElementalLoad
NodalLoad
SP_Constraint
fix
equalDOF
rigidDiaphragm
rigidLink
…
Plain
…
eleLoad
load
sp (prescribedNodalValue)
uniformExcitation
groundMotion

## Slide 5
Page 5
STKO
Domain
SP_Constraint
Timeseries
MP_Constraint
LoadPattern
LOGIC AND ABSTRACTIONS
ElementalLoad
NodalLoad
SP_Constraint
DEFINITIONS
CONDITIONS
+
node -mass
+ frictionModel
+ randomVariable

## Slide 6
Page 6
Creation and assignments
STKO
available operations
color coding
assignment
inclusion in Analysis steps
Not Used
Referenced
Not Used
Used
Referenced
no DRAG and DROP
target has to be selected BEFORE clicking OK
some conditions have restricted selection*
definitions are not assigned, just referenced in the loadPattern
*see slide 17
Mass: no need for referencing
Load: added in the loadPattern
Constraints: added in the constraintPattern

## Slide 7
Page 7
Definitions
What is a timeSeries in OpenSees?
Generally a timeSeries the relationship between the TIME in the domain, t, and the load factor applied to the loads, λ. Each timeSeries object is associated with a load Pattern object, which contains the loads to which is applied to factor λ.
timeSeries act differently depending on what type of object the are referenced to
(if associated with a uniformExcitation object, t is the acceleration or velocity
applied at the constrained DOF of the structure)
The same timeSeries can be reused for multiple analyses
It is particularly important to reset the pseudoTime in analysis with displacementControl as second stage, otherwise I would be using the 100% of the load of the first stage as the first load multiplier.
?

## Slide 8
Page 8
Definitions
What is time in OpenSees?
Time in OpenSees is called pseudoTime, it has a different meaning if you are performing a Static or Dynamic analysis.
Any analysis has to grow monotonically, in the dynamic analysis the time has the same meaning of real time, in static analysis is fictitious, it just means that the analysis is proceeding.
In Static analysis, in loadControl with a linear timeSeries, the
timestep can be considered as the loadmultiplier
In displacementControl the timestep is exactly the load
multiplier.

## Slide 9
Page 9
Definitions
timeSeries

## Slide 10
Page 10
Conditions
SP_Constraint
MP_Constraint
LoadPattern
Loads, constraints and masses
ElementalLoad
NodalLoad
SP_Constraint
CONDITIONS
fix
equalDOF
rigidDiaphragm
rigidLink
…
eleLoad
load
Node/Edge/Face/Volume Force
Node/Edge/Face/Volume Couple
+
surfaceLoad
…
sp
+
node -mass

## Slide 11
Page 11
Conditions
CONSTRAINTS
A constraint either prescribes the value of a DOF (as in imposing a support condition) or prescribes a relationship among DOF.
Single-point constraint
a single DOF is set to a known value
(often zero)
Multi-point constraint
a relationship between the DOF of two
or more nodes is imposed
applied to the geometry
applied to interactions

## Slide 12
Page 12
Conditions
Single-point constraints
fix $nodeTag (ndf $constrValues)
single-point homogeneous boundary constraints
$nodeTag
ndf $constrValues
dir1
dir2
dir3
dir4
dir5
dir6

## Slide 13
Page 13
Conditions
Multi-point constraints: equalDOF
equalDOF $rNodeTag $cNodeTag $dof1 $dof2 …
the DOF at the constrained node move exactly
he same as the DOF at the retained node
$rnodeTag
$cnodeTag
$dof1…
(dispc = dispr)

## Slide 14
rigidDiaphragm $perpDirn $rNodeTag $cNodeTag1…
constrains certain DOF at the listed constrained nodes to move
as if in a rigid plane with the retained node
Page 14
Conditions
Multi-point constraints: rigidDiaphragm
$perpDirn
$rNodeTag
$cNodeTag1
$cNodeTag2
$cNodeTag3
$cNodeTag4
In STKO you can create more rigidDiaphragms with the same interaction and condition
(dispc = dispr + rotr*dist)

## Slide 15
rigidDiaphragm $perpDirn $rNodeTag $cNodeTag1…
constrains certain DOF at the listed constrained nodes to move
as if in a rigid plane with the retained node
Page 15
Conditions
Multi-point constraints: rigidDiaphragm
A rigidDiaphragm imposes a condition of zero axial strain on the element connecting the constrained nodes.
For sections where the neutral axis does not shift as a consequence of bending in the beam this constraint has no effect on the axial load in the beam (elastic or steel sections).
For sections where the neutral axis does shift (RC fiber sections under moment) the moments in an unconstrained beam will cause the beam to undergo axial deformation. To constrain this axial deformation requires axial forces, the magnitude of which can be significant..

## Slide 16
rigidDiaphragm $perpDirn $rNodeTag $cNodeTag1…
constrains certain DOF at the listed constrained nodes to move
as if in a rigid plane with the retained node
Page 16
Conditions
Multi-point constraints: rigidDiaphragm
Ex. RC structure
Distributed plasticity beams (fiber sections)
Finite length plasticity columns (elastic sections)
See support file: ex15.scd and Massimo’s webinar

## Slide 17
rigidLink $type $rNodeTag $cNodeTag
constrains certain DOF at the listed constrained nodes to move as a rigid body
Page 17
Conditions
Multi-point constraints: rigidLink
equalDOF and rigidLink behave the same if there is no distance between the retained and constrained node
$type
$rnodeTag
$cnodeTag
(same as rD
for 2 nodes)

## Slide 18
Page 18
Conditions
Loads
load $nodeTag (ndf $LoadValues)
to construct a NodalLoad object and add it to the enclosing LoadPattern
Switching between conditions with different restricted selections will make you lose your target.

## Slide 19
Page 19
Conditions
Loads
load $nodeTag (ndf $LoadValues)
to construct a NodalLoad object and add it to the enclosing LoadPattern

## Slide 20
Page 20
Conditions
Loads
eleLoad -ele $eleTag1.... -type -beamUniform $Wy $Wz <$Wx>
to construct an ElementalLoad object and add it to the enclosing LoadPattern
$eleTag1
$Wx
$Wy
$Wz
specific for beams, especially when discretized to one element

## Slide 21
Page 21
Conditions
Loads
load $nodeTag (ndf $LoadValues)
eleLoad -ele $eleTag1.... -type -beamUniform $Wy $Wz <$Wx>

## Slide 22
Page 22
Conditions
Loads (prescribed displacement)
sp $nodeTag $dofTag $dofValue
construct a single-point constraint object and add it to the enclosing LoadPattern
$nodeTag
$dofTag
$dofValue

## Slide 23
Page 23
Conditions
Mass
mass $nodeTag (ndf $massValues)
Masses don’t need to be references in the Analysis steps
YOU NEED MASSES FOR EIGENVALUE AND DYNAMIC ANALYSIS!!!!

## Slide 24
Page 24
RESOURCES & REFERENCES
R&R
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Nonlinear finite element formulations
        A tale of two element formulations
        Numerical integration options
        Massimo’s OpenSees support group
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos

## Slide 25: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick