## Slide 1
Contents:
Simple frame structure
  Frame modelling
  Fiber cross section
  Refinement and fracture energy regularization
Add nonlinear shear in section aggregator
Add beam axial release
  Rigid diaphragm -> large axial compression in beams
  How to use HingedBeam compound element in STKO
Add nonlinear beam-column joint
  How to add interactions, rigid links and zero length springs
Download latest STKO version at: https://asdeasoft.net/?stko-trial
Download webinar support files at: https://asdeasoft.net/?stkowebinars-for-opensees

## Slide 2
Fracture energy regularization

## Slide 3
Shear in section aggregator

## Slide 4
tJ
gjoint
t
g
t
CRACKING
PRE-PEAK
PEAK
RESIDUAL
Envelope - exterior
Envelope - interior
backbone point | tj | gjoint (De Risi et al. 2016) | gjoint (Celik and Ellingwood, 2008)
cracking |  | 0.40‰ | 0.07‰
pre-peak | 0.95 tmax (J failure) - tj,y (BJ o CJ failure) | 1.70‰ | 0.60%
peak |  | 4.90‰ | 2.00%
residual | 0.43 tmax | 3.93% | 6.50%
(Uzumeri 1977)
(Jeon et al. 2015)
tmax = -0.586(TB)0.774 (BI)0.495 (JP)1.25(fc)0.941
Nodes A & A’
coinciding
Uzumeri, S. M. (1977). Strength and ductility of cast-in-place beam-column joints. In From the American Concrete Institute Annual Convention, Symposium on Reinforced Concrete Structures in Seismic Zones, San Francisco, 1974. (No. SP-53 Conf Paper).
J.S. Jeon, L.N. Lowes, R. DesRoches, I. Brilakis. Fragility curves for non-ductile rein-forced concrete frames that exhibit different component response mechanisms. Engineer-ing Structures, 85, 127-143, 2015.
M.T. De Risi, P. Ricci, G.M. Verderame. Modelling exterior unreinforced beam-column joints in seismic analysis of non-ductile RC frames. Earthquake Engineering and Struc-tural Dynamics, 46(6), 899-923, 2017.
O.C. Celik, B.R. Ellingwood. Modeling beam-column joints in fragility assessment of gravity load designed reinforced concrete frames. Journal of Earthquake Engineering, 12(3), 357-381, 2008
Beam-Column joints