## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
30
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28 April 2021
Introduction to OpenSees
05 May 2021
Introduction to STKO – Scientific Toolkit for OpenSees
June-October (once a week)*
Model definition overview
Geometry, Interactions, Selection sets, Local axes Physical properties
Element properties
Definitions and Conditions
Mesh and Analysis (2 hours on the Analysis Commands)
Postprocessing and results visualization
Modal and response spectrum analysis
Linear, nonlinear static and dynamic analysis
Reinforced concrete and masonry frame structures
(+ softening and mesh objectivity, diaphragms modelling, joints modeling, infill panels…)
*Only one in August
1
2
3
4
11
12
20
Full syllabus available here
THEORY
PRACTICE
INTRO

## Slide 3
GET STARTED in OpenSees with STKO
Introduction
to STKO
Scientific Toolkit for OpenSees
2
What?
Definition
Why?
OpenSees | STKO
Python
HDF5 database
MPCO recorder
How?
Motivation
Applications
Potential
W1 review + more TCL
STKO basics
05 May 2021
Introduction to STKO
2
Python basics
Assignment (NEW!)
Installation
More R&R
Example in STKO

## Slide 4
Page 4
= Scientific ToolKit for OpenSees
What?
DEFINITION
Visit our website: https://asdeasoft.net/?product-stko
“STKO is a cutting-edge complex data visualization tool for
OpenSees, it creates an input and output file readable with its advanced openGL graphic interface
for both pre and post processing.
It includes ALL materials, elements, conditions, and interactions offered in OpenSees, providing you with the
ability to harness the power of OpenSees and to take advantage of its full potential.”

## Slide 5
“STKO is a cutting-edge complex data visualization tool for
OpenSees, it creates an input and output file readable with its advanced openGL graphic interface
for both pre and post processing.
It includes ALL materials, elements, conditions, and interactions offered in OpenSees, providing you with the
ability to harness the power of OpenSees and to take advantage of its full potential.”
Page 5
= Scientific ToolKit for OpenSees
What?
DEFINITION
Visit our website: https://asdeasoft.net/?product-stko
Graphic User Interface
model definition and analysis setup
results visualization and extraction
OpenSees but BETTER
Tcl
HDF5 database
YOU CAN SEE WHAT YOU ARE CODING!!!

## Slide 6
MOTIVATIONS (Why do you need STKO?)
Why?
  OpenSees limitations
  controlling the modeling of complex structures is difficult
  manual coding can be time consuming and not accessible to all
  handle manually high-volume output data
  lack of visualization tools for results (fibers)
Page 6
STKO pre-processor
open box scriptable GUI to control and produce input files
STKO post-processor
manipulate and visualize large volume of complex data
  Verification & Validation
To know more: www.nafems.org

## Slide 7
Page 7
APPLICATIONS (FE code – use and possibilities)
Why?
OTHERS
SEISMOSTRUCT
SAP2000
ETABS
MIDAS
ABAQUS DIANA FEA
ROBOT
Black Box
Linear and nonlinear
Automatic mesh algorithms
Scripting capabilities (Python, Fortran, …)
Open Box
Open-source framework
No mesh algorithms
No GUI
Full scripting capabilities (tcl)
Black Box
Linear with some basic nonlinearities
Automatic checks and drawings
BIM (ifc or proprietary)
Some with API
Black Box
Linear
Automatic checks
and drawings
BIM (ifc or proprietary)
High level professionals
Research limited
Professionals (limited)
Research limited (no GUI)
Professionals
Basic research
Professionals
No research
High level professionals Research oriented with GUI

## Slide 8
Page 8
POTENTIAL
Why?
learn and understand OpenSees
(input Tcl files generation)
visualize and control pre- and post-processing
advanced CAD Modeling (import export open file formats)
embedded meshing algorithms
(no need for user implementations)
mesh-partitioner
(access to multi processors analysis for large models)
material tester
add support for new OpenSees components
(materials, elements, etc..)
create automations (automatic beam-column joints)
customize post-processing
(create and visualize derived results)

## Slide 9
Page 9
OPENSEES
How?
constructs objects
holds state ti
(then (ti+dt) when moved)
stores
Domain
Modelbuilder
Analysis
adds
moves the state
from ti to (ti+dt)
monitors
provides access
Recorder
| STKO pre-processor
Recorder
MPCO
reads
STKO post
processor
creates and
visualizes results
STKO follows OpenSees abstractions

## Slide 10
Page 10
How?
Element
Domain
Node
SP_Constraint
Timeseries
MP_Constraint
LoadPattern
OPENSEES
| STKO pre-processor
Mesh
Geometry
Interactions
Physical properties
Element properties
Conditions
Definitions
Analysis
Analysis
steps

## Slide 11
Page 11
How?
OPENSEES
| STKO pre-processor
Workplanes
Local axes
Selection sets
Geometry
Interactions
(+ Mesh)
Open-source
(Python)
Closed-source (C++)
Definitions
Physical properties
Element properties
Conditions
Analysis steps
C:\Program Files\STKO\external_solvers\opensees

## Slide 12
Page 12
The Python SCRIPTING INTERFACE
How?
Use of Python interpreter to write automations, new components, interact
with STKO pre-post processor environment, etc…
C:\Program Files\STKO\external_solvers\opensees
X-Object components customizable by the users, linking STKO with OpenSees
Custom component in OpenSEES
ConcreteDamage.dll
Write a X-Object to link with STKO
ConcreteDamage.py
Automations
Interaction with the pre- and
post- processor through the API

## Slide 13
Page 13
HDF5 Output Database
How?
open source
portable
no limits
wide range of computational platforms and programming languages
parallel I/O
hierarchical structure
groups (directories)
datasets (data)
attributes (metadata)
Hierarchical Data Format
a set of file formats designed to store and organize large amounts of data
To know more about HDF5:
https://hdfgroup.org
HDFView to see inside an .mpco file

## Slide 14
Page 14
MPCO Recorder
How?
Model (+ model stages)
  nodes
  elements
    geometries + standard and custom integration rules
  sections and materials + assignments
Results
  results stored on nodes
  results stored on elements
    on element nodes
    on integration points
    on sub-integration points (fibers)
fiber plots
multi stages
…
Multi Purpose CAE Output - new recorder class
Implementation of an HDF5 database in OpenSees
C:\Program Files\STKO\documentation\PDF\MPCORecorder.pdf

## Slide 15
Page 15
To keep in mind before moving forward!
OpenSees vs 🌏
the order in which you input commands matters but it’s flexible
you are literally building up your model
timeSeries definition
the same concept is used to represent load multipliers (static analysis) and the time steps (dynamic)
concept of Conditions
everything you apply as a static or kinematic condition on your model
potential for automation
tbh…OpenSees is not intended to make your life easier, but to give you more power!
You are the programmer!
No self-weight automatic implementation
No load multipliers
No preloaded materials and elements preloaded libraries
No present options for supports and loading conditions
both a powerful modeling tool and an excellent learning tool
What else???

## Slide 16
INSTALLING STKO
Installation
Windows
Page 16
STKO does NOT embed OpenSees
(you need to have OpenSees already installed)
Log in
Download – just a suggestion: OpenSees 3.2.2 compiled by prof. Nicola Tarque PUCP (unofficial version)
Download – STKO version 2.0.2
for licensing issues: first check the installation guide
then WRITE TO info@asdeasoft.net (with your CUSTOMER-ID)
File formats
      .scd (your model, your cae document, what you don’t want to erase!)
      .spd (your post-processor file, saves plot groups, charts, etc…)
      .mpco (your output database, the solution of your model to load in the post-processor)
      .mpco.data (some data of your model, you don’t need this…)
      Create a folder for your modelling
      You are in!
Where to buy:
https://asdeasoft.net/?stko-purchase
Installation guide:
https://asdeasoft.net/pdf/STKO%20Installation%20guide.pdf

## Slide 17
STKO interface
STKO Basics
Page 17
Check out our manual: https://asdeasoft.net/pdf/_STKO%20Manual_.pdf
Editor Windows
Terminal
Work Tree
Render window
Quick Access Toolbar
Main Menu
Main Toolbar
Interface Switch
Scripting interface
Editor
Notes: Pre-post
3 ways to call commands
Python API

## Slide 18
Page 18
STKO basics
OPENSEES
| STKO pre-processor
from here you have access to your script with the customCommand
Here the order does not matter
Here it DOES!

## Slide 19: «OpenSees does NOT have the concept of unit system»
See support file from WEEK 1: utils0.tcl
0
DAYS
Since the last unit mistake on the forum
(I am counting my mistakes too!)

## Slide 20
Page 20
Unit System
Consistent Units |  |  |  | 
Length | m | mm | ft | in
Time | s | s | s | s
Mass | kg | ton | lbf × s2/ft | lbf × s2/in
Force | N | N | lbf | lbf
Temperature | C | C | F | F
Velocity | m/s | mm/s | ft/s | in/s
Acceleration | m/s2 | mm/s2 | ft/s2 | in/ s2
Angular velocity | rad/s | rad/s | rad/s | rad/s
Density | kg/m3 | ton/mm3 | slug/ft3 | lbf × s2/in4
Moment | N × m | N × mm | ft × lbf | in × lbf
Stress | Pa | Mpa | psf | Psi
Energy | J | mJ | ft × lbf | in × lbf
g-Gravity Constant | 9.81E+00 | 9.81E+03 | 3.22E+01 | 3.86E+02
Steel Density | 7.83E+03 | 7.83E-03 | 1.52E+01 | 7.33E-04
Steel Modulus | 2.07E+11 | 2.07E+05 | 4.32E+09 | 3.00E+07

## Slide 21
N1
N4
N2
N3
E1
E2
E3
Page 21
W1 EXAMPLE (2D portal frame distributed load) review and more TCL
more Tcl basics
See support file: ex2bis.tcl and ex2tris.tcl
Reference system
N-m-s
H = 3m
l = 4 m
square section
b = 300 mm
E = 2.0e+5 MPa
p = 1000 N
From 2d to 3D
Use the mpco recorder
Output files in a specific directory
Create a loop to replicate the structure
W1 REVIEW
https://www.tutorialspoint.com/execute_tcl_online.php
x
y
11
21
31
41
12
22
32
42
13
23
33
43

## Slide 22
PYTHON BASICS
Python Basics
Page 22
C:\Program Files\STKO\python.exe
python version 3.6.6
Data types
(text, numeric, sequence, mapping, booleans, etc…) - not everything is string here as in tcl
Display info print
Variables(definition, substitution, operations (arithmetic, assignment, logical, etc..)
Data type casting
Control structures if, while, for, foreach
Functions def ()
Object oriented programming (classes) class ()
File manipulation and sourcing open
Importing external packages import
There is an STKO specific Python Package: PyMpc
Check out Python official documentation:
https://docs.python.org/3/tutorial/index.html
Check out PyMpc documentation
Notes: Interfaccia dai tutorial

## Slide 23
Page 23
EXAMPLE (2D portal frame distributed load) in STKO
Example (STKO)
See support file: ex3.scd and utils_1.py
Model setup
Simple python script to define an attribute value
Result comparison with ex2bis.tcl
Notes: Write tcl
Show HDF viewed the database
Python API

## Slide 24
Page 24
NEW ASSIGNMENT
Assignment
STKO: Tryout making the same tcl example you picked from week 1 back in STKO, just exploring the software
(one that you know already how to solve analytically)
Write the tcl file of your model with the command WriteTCL.
Write a python support file just for calculations, maybe analytical comparison and run it.
Load your database file.
TCL: Complete the 3D frame example started with ex2tris.tcl
Create a larger frame structure using loops and lists.
Run it in OpenSees.
Load the mpco database file in STKO to check your geometry.

## Slide 25
Page 25
MORE RESOURCES & REFERENCES
R&R
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog

## Slide 26: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick