## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
60
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28/04/21 – 05/05/21
Introduction to OpenSees
Introduction to STKO – Scientific Toolkit for OpenSees
Model definition overview
Geometry, Interactions, Selection sets, Local axes
Physical properties
Element properties
Definitions and Conditions
Mesh and Analysis
June-October (once a week)*
Analyses Command (part 1-2)
Analyses Command (part 3-4) - 28/07/2021
Postprocessing and results visualization
Modal and response spectrum analysis
Linear, nonlinear static and dynamic analysis
Reinforced concrete and masonry frame structures
(+ softening and mesh objectivity, diaphragms modelling, joints modeling, infill panels…)
*Only one in August
1
2
9
11
12
20
Full syllabus available here
THEORY
PRACTICE
INTRO
3
4
5
6
7
x2
5:30 p.m.
CEST
8

## Slide 3
GET STARTED in OpenSees with STKO
AnalysesCommand
9
21 July 2021
AnalysesCommand
9
AnalysesCommand
Constraint handlers
Numberers
Convergence test
System solvers
Solution algorithms
Next week, specific setup for STATIC and TRANSIENT analyses
DISCLAIMER

## Slide 4
provide the solution
numbers
the dof
determines the next time step for an analysis
iterates from the last time step to the current
tests the convergence
of the solution
handles the constraints
defines the type of analysis
CTest
SolnAlgorithm
Integrator
Solver
Numberer
CHandler
Analysis
AnalysisModel
OpenSees abstraction
AnalysesCommand
Page 4

## Slide 5
AnalysesCommand – default settings
AnalysesCommand
Page 5
recorder
constraintPattern
loadPattern
AnalysesCommand
1
2
3
4
Basic generic setup
Constraint Handler
Numberer
System solver
Solution algorithm
Convergence test

## Slide 6
Constraint
Handlers

## Slide 7
Definition
Constraint Handler
Page 7
The ConstraintHandler object determines how the constraint equations are enforced in the analysis. It’s how OpenSees applies the boundary conditions to the system matrix.
Constraint equations enforce
a specified value for a degree-of-freedom,
or a relationship between degrees-of-freedom.
In relationships between DOFs, they are distinguished between retained (master) and constrained (slaves), at times this distinction is relevant
(e.i. RigidDiaphragm), in other instances they are interchangeable
(e.i. equalDOF).
Wrong HANDLERS can lead to singularities
handles the constraints

## Slide 8
Types of constraints handlers
Constraint Handler
Page 8
Plain Constraints
Lagrange Multiplier
Transformation
Penalty Method
4 Options
choice of the user
The four options differ on:
the way they transform the system matrix
If they can handle non-homogenous constraints ( ≠ 0)
If they can handle multi-point constraints (not identity matrices)
If they distinguish retained and constrained pair
If they can be used with specific convergence test

## Slide 9
Plain Constraints
Constraint Handler
Page 9
MATRIX CONDENSATION
Plain Constraints
Lagrange Multiplier
Transformation
Penalty Method
same matrix condensation
Constraints are handled by matrix condensation, erasing some of the DOFs from the global stiffness matrix, reducing its size.
In this case, the degrees of freedom can be broken down into UR, the retained DOF's, and UC, the condensed DOF’s.
In this case it is important to pay attention to the retained and constrained pairs, which node is which.
If a node is constrained by two different retained node, once it is erased for the first time, it will not be available to enforce the second condition.

## Slide 10
Plain Constraints
Constraint Handler
Page 10
LIMITATIONS
Plain Constraints
Lagrange Multiplier
Transformation
Penalty Method
Enforces only homogeneous single-point constraints (= 0), such as the case of homogeneous boundary conditions, where all boundary conditions are fixity, using single-point constraints. It cannot be used for imposed displacements or rotations.
Only for constraints that had an identity matrix, every single point constraint is fixing an element on the diagonal. No multi-point constraints as they all produce matrices which are not diagonal (except the equalDOF).
equalDOF (dispc = dispr)
rigidDiaphragm (dispc = dispr + rotr*dist)
rigidLink (same as rD for 2 nodes)

## Slide 11
Lagrange Multiplier
Constraint Handler
Page 11
Plain Constraints
Lagrange Multiplier
Transformation
Penalty Method
MATRIX “MULTIPLICATION”
+
Constraints are handled by enlarging the size of the global stiffness matrix, there is no condensation here. Instead one equation is added for each constraint that needs to be enforced. Once Lagrange Multipliers are applied, the stiffness matrix is transformed, if it was originally symmetric positive definite it will no longer be.
This can be an issue in the choice of system solver.
Symmetric Positive Definite (SPD) are characteristics the structure global stiffness matrix can have. Positive definite means that contains only strictly positive finite eigenvalues. A model is not always positive definite. It can be if it’s elastic, or has strain-hardening behaviour. If there is softening or non-associated plasticity the matrix won’t be positive definite.

## Slide 12
Lagrange Multiplier
Constraint Handler
Page 12
LIMITATIONS
Retained-constrained pairs are important also here, if there is a constrained node referencing two retaining nodes, two constraint equations will be created, which are linear dependent, creating a singularity.
There would also be a problem is the system would be over-constrained, but this does not create a singularity, as OpenSees does takes care of it (you may lose important constraints though).
You cannot use a convergence test on the displacement with this handler. In the new rows added to the stiffness matrix, the solution vector (displacement and rotation vector) contains also forces which change the order of magnitude of the vector. It is hard to reach convergence with a tolerance on displacement that needs to be applied to forces too.
Plain Constraints
Lagrange Multiplier
Transformation
Penalty Method

## Slide 13
Transformation
Constraint Handler
Page 13
Plain Constraints
Lagrange Multiplier
Transformation
Penalty Method
MATRIX CONDENSATION
Constraints are handled here as for the Plain Constraints with less limitations. There is condensation of the matrix, which is reduced in size. This is the most general handler choice, it can be used with non-homogenous constraints too.
The ONLY LIMITATION is in reference to retained-constrained pairs, and nodes constrained in series.

## Slide 14
Penalty Method
Constraint Handler
Page 14
Plain Constraints
Lagrange Multiplier
Transformation
Penalty Method
Constraints are enforced with the penalty method. This method consists of adding large numbers to the stiffness matrix and restoring the force vectors to impose a prescribed displacement o nonzero DOF. It works numerically rather than adding or erasing rows in the matrix. This additional stiffness affect the eigenvalues/vectors in a transient analysis, therefore the choice of parameters is paramount.
The matrix size remains the same, the penalty method does not change the system size.
MATRIX TRANSFORMATION

## Slide 15
Penalty Method
Constraint Handler
Page 15
Plain Constraints
Lagrange Multiplier
Transformation
Penalty Method
It is not possible to use the Norm Unbalance Convergence Test, as the addition of very stiff springs will never bring the constrained forces to zero and it will be very difficult to pass a small tolerance in terms of forces.
The choice of the penalty parameters should be done accurately, and if possible in comparison with another handler. The highest stiffness order of magnitude in the model should be incremented up to 8 (be aware of the stiffness units).
LIMITATIONS
LARGEST STIFFNESS MAGNITUDE + 8
(relevant number of digits in a byte)
Parameters should be large enough to effective, but not too large to cause numerical difficulties.

## Slide 16
Comparison
Plain
matrix transformation
Constraint Handler
Page 16
non-homogeneous
constraints
mp constrained
retained-costrained
pairs
convergence
test
Lagrange
Transformation
Penalty
does not change the system size
condensate slave DOFs
adds 1 row for each constraint equation
condensate slave DOFs
can not enforced
can be enforced
can be enforced
can be enforced
pay attention
pay attention
pay attention
no problem
can not enforced
can be enforced
can be enforced
but not in series
can be enforced
no problem
no Norm Displacement Test
no problem
no Norm Unbalance Test
Check out the OpenSees manual

## Slide 17
Which one should you use?
Constraint Handler
Page 17
Plain Constraints
Lagrange Multiplier
Transformation
Penalty Method
only if you don’t have mpconstraints or prescribed displacements or rotation
always when you have mpconstraints, by pay attention at penalty parameters
only if you don’t expect a large global matrix already
always, unless mixed retained-constrained pairs, or constrains in series

## Slide 18
Common errors
Constraint Handler
Page 18
There is no unique choice, no HANDLER will work in any case!
    The constraints are not enforced as you modelled them
          (they can be skipped, and you could see unexpected results)
          The matrix is singular and there is a warning
          (OR NOT! e.i. Plain Constraints against Transformation)
Check out the
Massimo’s webinar

## Slide 19
Numberers

## Slide 20
Definition
Numberer
Page 20
The DOF_Numberer object determines the mapping between equation numbers and degrees-of-freedom -- how degrees-of-freedom are numbered.
Renumbering allows to concentrate relevant information around the diagonal of the global stiffness matrix and obtain sparse matrices (matrices that allocate only the non-zero values in the machine memory), reducing the computational cost of the analysis. Sparse matrices are necessary to run large models.
e.i. 1000 nodes * 6 DOFs ^ 2 * 8 bytes ≈ 300MB
+ space for matrix transformation, factorization, results…...
numbers the DOFs

## Slide 21
Types of Numberers
Numberer
Page 21
Plain
Reverse CuthillMcKee (RCM)
Alternative_Minimum_Degree
Parallel RCM
small problems or for sparse solvers, no internal DOFs numbering system
rr if you wish to print the global matrix (only with FullGeneral solver – printA function)
RCM for parallel analysis
large problems, builds a sparse matrix than can optimize factorization and cut on computational cost
not much used
Nodes are assigned degrees-of-freedom arbitrarily, based on the input file. The user has no control.
Optimizes node numbering to reduce bandwidth using a numbering graph.

## Slide 22
System solvers

## Slide 23
Definition
System solver
Page 23
The system solver constructs the linear system of equations LinearSOE, and LinearSolver object, to store and solve the system of equations for the solution of the boundary value problem. It provides the solution of the differential equations.
The problem matrices has to respect the characteristics available in the solver.
provides and stores
the solution
Profile SPD
Banded SPD
Sparce SPD
Banded General
Sparse Asymm nPD

## Slide 24
Types of solvers
System solver
Page 24
BandGeneral
Lapack band general solver for band matrices
BandSPD
Lapack band spd solver for SPD matrices
ProfileSPD
Profile solver for SPD matrices
SuperLU
For sparse and asymmetrical matrices
(e.i. non-associated plasticity, DamageTC3D without the IMPLEX algorithm)
UmfPack
For sparse and asymmetrical matrices, faster than the SuperLU
SparseSYM SOE
For sparse by symmetric matrices
Mumps
Parallel computing
Very fast (1 partion not in parallel)
Cusp
Linear sparse solver for sparse matrices, runs on the GPU
ParallelProfileSPD
Profile solver for parallel computing of SPD matrices
FullGeneral
Only for small models, if you want to print the global matrix. It should almost never be used!, because it requires a lot more memory than every other solver and takes more time in the actual solving operation than any other solver.

## Slide 25
Solution algorithms

## Slide 26
Definition and types
Solution Algorithm
Page 26
determines the next step
The solution algorithm determines the sequence of steps taken to solve the non-linear equation system.
Linear
For linear problems
Newton
Newton-Raphson NR algorithm
Newton with Line Search
Newton with improved convergence
Modified Newton
Newton with initial stiffness (faster but less accurate)
Krylov-Newton
Often used with softening behaviour, faster analysis, can ask to update the matrix at a specific interval, helps with instability.
Quasi-Newton or Secant
Newton with secant stiffness
BFGS Algorithm
Broyden Algorithm
Diagrams are an elaboration from SAHC2019 lecture notes (Milan Jirásekv and Paulo B. Lourenço).

## Slide 27
Convergence
Tests

## Slide 28
Definition and types
Convergence Test
Page 28
tests the convergence
Determines if the convergence has been achieved at the end of each iteration step, against a specific tolerance.
Norm Unbalance
Test on forces equilibrium
Not with the Penalty Handler
Norm Displacement Increment
Test on displacement coherence
Not with Lagrange Multipliers
Energy Increment
Test on energy, which comes down to a product of forces * displacements
Relative Norm Unbalance
Relative Norm Displacement
Relative Energy Increment
Ratio of the error at the time step against the initial error
Total Relative Norm Displacement Increment
Fixed number of iteration

## Slide 29
Common errors
Convergence Test
Page 29
    Be careful with your units, and with relative tests, to the unit of the initial step error.
          (the tolerance is applied to the results obtained, if you are modelling in mm a Norm Displacement Increment Test with a tolerance of 10e+9, it’s never going to converge!)
          If you are using Energy tests, your convergence will be improved (as they are less restrictive), but be careful with units of different magnitude orders (kN and mm for example)
    Combination CONSTRAINT HANDLER and CONVERGENCE TEST.

## Slide 30
Page 30
RESOURCES & REFERENCES
R&R
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Nonlinear finite element formulations
        A tale of two element formulations
        Numerical integration options
        Massimo’s OpenSees support group
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos

## Slide 31: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick