## Slide 1: Modeling of Bolted Steel Connections
Onur Deniz Akan
onurdeniz.akan@unich.it
June 25, 2025

## Slide 2: Outline
Bolts
Bolted connections
Drawing bolt hole geometry
Bolt component models
Model applications in STKO
  T-stub tension
  Quad-bearing
  T-Joint sub-model
Q&A
Proper meshing is important for contact!
Liu, Yang & Liu, Kun & Wang, Wentao & Fan, Linlin & Binbin, Li. (2024). Progress on the connection performance of steel-engineered bamboo beam- column connections under cyclic loads: a review. Sustainable Structures. 4. 37. 10.54113/j.sust.2024.000037.

## Slide 3: AISC 360 – Bolted Joints (S. J3)
ANSI/AISC 360 | American Institute of Steel Construction
From the link
Bolt Types & Usage
  Common Bolts: ASTM A307 permitted unless pretensioning is needed.
  High-Strength Bolts:
    Classified by minimum tensile strength (ksi):
      Group 120: A325, F1852
      Group 144: F3148
      Group 150: A490, F2280
      Group 200: F3043, F3111
  Correct classification ensures proper strength and code compliance.

## Slide 4: Design properties for metric hex bolts
 | Dimensions |  | Hole diameter d0 [mm] |  |  |  | Areas |  | Tensile resistance Ft,Rd [kN] |  |  |  |  |  |  | Shear resistance per shear plane Fv,Rd [kN] |  |  |  |  |  | 
Size | Nominal diameter d [mm] | Nut width across flats s [mm] | Normal round hole | Oversize round hole | Short slotted hole | Long slotted hole | Gross area (unthreaded part) Ag [mm2] | Stress area (threaded part) As [mm2] | 4.6 | 4.8 | 5.6 | 5.8 | 6.8 | 8.8 | 10.9 | 4.6 | 4.8 | 5.6 | 5.8 | 6.8 | 8.8 | 10.9
M8 | 8 | 13 | - | - | - | - | 50.3 | 36.6 | 10.5 | 10.5 | 13.2 | 13.2 | 15.8 | 21.1 | 26.4 | 7.03 | 5.86 | 8.78 | 7.32 | 8.78 | 14.1 | 14.6
M10 | 10 | 16 | - | - | - | - | 78.5 | 58.0 | 16.7 | 16.7 | 20.9 | 20.9 | 25.1 | 33.4 | 41.8 | 11.1 | 9.28 | 13.9 | 11.6 | 13.9 | 22.3 | 23.2
M12 | 12 | 18 | 13 | 15 | 16×13 | 30.0×13 | 113 | 84.3 | 24.3 | 24.3 | 30.3 | 30.3 | 36.4 | 48.6 | 60.7 | 16.2 | 13.5 | 20.2 | 16.9 | 20.2 | 32.4 | 33.7
M14 | 14 | 21 | 15 | 17 | 18×15 | 35.0×15 | 154 | 115 | 33.1 | 33.1 | 41.4 | 41.4 | 49.7 | 66.2 | 82.8 | 22.1 | 18.4 | 27.6 | 23.0 | 27.6 | 44.2 | 46.0
M16 | 16 | 24 | 18 | 20 | 22×18 | 40.0×18 | 201 | 157 | 45.2 | 45.2 | 56.5 | 56.5 | 67.8 | 90.4 | 113.0 | 30.1 | 25.1 | 37.7 | 31.4 | 37.7 | 60.3 | 62.8
M18 | 18 | 27 | 20 | 22 | 24×20 | 45.0×20 | 254 | 192 | 55.3 | 55.3 | 69.1 | 69.1 | 82.9 | 110.6 | 138.2 | 36.9 | 30.7 | 46.1 | 38.4 | 46.1 | 73.7 | 76.8
M20 | 20 | 30 | 22 | 24 | 26×22 | 50.0×22 | 314 | 245 | 70.6 | 70.6 | 88.2 | 88.2 | 105.8 | 141.1 | 176.4 | 47.0 | 39.2 | 58.8 | 49.0 | 58.8 | 94.1 | 98.0
M22 | 22 | 34 | 24 | 26 | 28×24 | 55.0×24 | 380 | 303 | 87.3 | 87.3 | 109.1 | 109.1 | 130.9 | 174.5 | 218.2 | 58.2 | 48.5 | 72.7 | 60.6 | 72.7 | 116.4 | 121.2
Table of design properties for metric steel bolts M5 to M39 - Eurocode 3

## Slide 5: AISC 360 – Bolted Joints (S. J3)
Slip-Critical Connections
These rely on friction between the connected surfaces.
No slip is allowed at service load. (Good for fatigue…)
Requires bolt pre-tensioning. (using special equipment)
Bearing (Shear) Connections
The bolts are designed to bear against the sides of the holes as the load is transferred.
Some slip may occur, but it is acceptable under service loads.
Subdivided into
  Bearing-Strength Controlled
  Shear-Strength Controlled
Tension Connections
Bolts are loaded in tension (axial force), relatively small shear.
Common in splice connections or hangers.
Must consider bolt tensile strength and prying action.
Can be modeled with shells and bolt component elements!
Full solid - Bricks!!

## Slide 6: Bolt Hole Geometry 1
M18 Bolt
9 mm
13.5 mm

## Slide 7: Bolt Hole Geometry 2

## Slide 8: Bolt component models
Simple Bolt Component (Good for tension)
Detailed Bolt Component (Good for bearing-shear)
Node
Node
zeroLength element
Axial – uniaxialMaterial (Steel)
Shear – uniaxialMaterial (Hysteretic)
Rest – uniaxialMaterial (Elastic-rigid)
Plate Node
Rigid links
Contact elements (with rigid gap)
Rigid shell elements
Rigid links
Elastic BeamColumn element
zeroLength element
Elastic BeamColumn element

## Slide 9: T-Stub Tension Joint

## Slide 10: Double-Bolted Bearing

## Slide 11: T-Joint Sub-model