## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
30
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28/04/21 – 27/10/2021
Introduction to OpenSees
Introduction to STKO – Scientific Toolkit for OS
Model definition overview
Geometry, Interactions, Selection sets, Local axes
Physical properties
Element properties
Definitions and Conditions
Mesh and Analysis
Analyses Command (part 1-2)
Analyses Command (part 3-4)
Postprocessing and results visualization
Linear elastic analysis
Material and geometrical nonlinearities
Modal and response spectrum analysis
Nonlinear static and dynamic analysis
Reinforced concrete and masonry frame structures
(+ softening and mesh objectivity, diaphragms modelling, joints modeling, infill panels…)
1
2
13
20
Full syllabus available here
THEORY
PRACTICE
INTRO
3
4
5
6
7
8
9
10
11
12

## Slide 3
GET STARTED in OpenSees with STKO
Material and geometric nonlinearities
Nonlinear materials
Masonry
Steel
08 September 2021
Material and geometric nonlinearities
Concrete
13
12
Nonlinear geometry
geomTransf
Linear – Week 4
Pdelta
Corotational

## Slide 4
Page 4
NL Materials
Uniaxial materials
See OpenSees Manual
and prof. Scott blog post on «Uniaxial Multi-Tool»
UniaxialMaterial objects in OpenSees can represent relationships in terms of:
stress-strain
Truss elements
“stress and tangent are multiplied by cross-section area to get force and stiffness”
FiberSection objects
“stress and tangent are multiplied by fiber area to get fiber force, which is summed over the section to get section stress resultants (axial force and bending moment)”
force-strain
SectionAggregator (in a beam)
“no automatic integration of the model response, stiffness
and force necessary input”
force-displacement or moment-rotation
ZeroLength elements (springs)
“no automatic integration of the model response, stiffness and force/moment
necessary input”
σ-ε
F-ε
F-d
M-r

## Slide 5
Page 5
NL Materials
Elastic
uniaxialMaterial Elastic $matTag $E<$eta> <$Eneg>
linear behaviour
$matTag - material object tag
$E - tangent
$eta – damping tangent (default 0.0)
$Eneg – tangent in compression (default = E)
$epscu - strain at crushing strength
See OpenSees Wiki
(it is possible to use the section Elastic command directly or the elasticBeamColumn, this can be useful to assign specific stiffness parameters, e.g. to the rigid end of an hinged beam)
N-m-s

## Slide 6
Page 6
NL Materials
Concrete01
ZERO TENSILE STRENGTH
strain
stress
fpcu
fpc
epsc0
epscU
2*fpc/epsc0
INITIAL SLOPE
(concrete maximum compressive strength)
(concrete crushing strength)
parameters should be input as negative values (if input as positive, they will be converted to negative internally).
uniaxialMaterial Concrete01 $matTag $fc $epsco $fcu $epscu

## Slide 7
Page 7
NL Materials
Concrete01
DEGRADED LINEAR UNLOADING/RELOADING STIFFNESS
according to the work of Karsan-Jirsa
no tensile strength

## Slide 8
Page 8
NL Materials
Concrete02
LINEAR TENSION SOFTENING
strain
stress
fpcu
fpc
epsc0
epscU
E0 = 2*fpc/epsc0
initial slope
(concrete maximum compressive strength)
parameters should be input as negative values (if input as positive, they will be converted to negative internally).
Ets
ft
lambda*E0
[ratio between unloading slope at epscU and initial slope]
(concrete crushing strength)
[tension softening stiffness (absolute value)]
uniaxialMaterial Concrete02 $matTag $fpc $epsc0 $fpcu $epsU $lambda $ft $Ets
ft = 10% fpc
Ets = 10% fpc/epsc0
See prof. Scott’s post
lambda = 0.05÷ 0.2

## Slide 9
Page 9
NL Materials
Concrete02

## Slide 10
Page 10
NL Materials
Steel01
strain or deformation
stress or force
Fy
[yield strength]
uniaxialMaterial Steel01 $matTag $Fy $b $E0 <$a1 $a2 $a3 $a4>
Fy
E0
E0
b*E0
b*E0
KINEMATIC HARDENING
[strain-hardening ratio]
+ optional isotropic hardening described by a non-linear evolution equation

## Slide 11
Page 11
NL Materials
Steel01

## Slide 12
Page 12
NL Materials
Steel02
strain or deformation
stress or force
Fy
[yield strength]
Fy
E
E
b*E
b*E
KINEMATIC HARDENING
[strain-hardening ratio]
+ optional isotropic hardening described by a non-linear evolution equation
uniaxialMaterial Steel02 $matTag $Fy $E $b $R0 $cR1 $cR2 <$a1 $a2 $a3 $a4 $sigInit>
R0 = 10 ÷ 20
cR1 = 0.925
cR2 = 0.15
parameters to control the transition from elastic to plastic branches

## Slide 13
Page 13
NL Materials
Steel02
+ optional isotropic hardening described by a non-linear evolution equation

## Slide 14
Page 14
NL Materials
Hysteretic
uniaxialMaterial Hysteretic $matTag $s1p $e1p $s2p $e2p <$s3p $e3p> $s1n $e1n $s2n $e2n <$s3n $e3n> $pinchX $pinchY $damage1 $damage2 <$beta
strain or deformation
stress or force
s3p
THREE POINTS BACKBONE FUNCTIONS
s2p
s1p
s1n
s2n
s3n
e1p
e2p
e3p
e3n
e2n
e1n
K0
mu–beta*K0
[power used to determine the degraded unloading stiffness based on ductility]
+ PINCHING
opening and closing of cracks in cyclic loading
+ DAMAGE
cyclic strength and stiffness degradation (ductility or energy)

## Slide 15
Page 15
NL Materials
Hysteretic

## Slide 16
uniaxialMaterial Pinching4 $matTag $ePf1 $ePd1 $ePf2 $ePd2
$ePf3 $ePd3 $ePf4 $ePd4
$rDispP $rForceP $uForceP
Page 16
Materials
Pinching4
“pinched” load-deformation response
degradation under cyclic loading
$matTag
strain or deformation
stress or force
ePf3
FOUR POINTS BACKBONE FUNCTIONS
ePf2
ePf1
eNf1
eNf2
eNf3
ePd1
ePd2
ePd3
eNd4
eNd2
eNd1
+ three types of cyclic strength and stiffness degradation:
unloading stiffness degradation
reloading stiffness degradation
strength degradation
ePd4
ePf4
eNd3
eNf4
rDispP/N - ratio of the deformation at which reloading occurs to the maximum/minimum historic deformation demand
fForceP/N - ratio of the force at which reloading begins to force corresponding to the maximum /minimum historic deformation demand
uForceP/N - ratio of strength developed upon unloading from negative load to the maximum/minimum strength developed under monotonic loading
[*,uForceN*eNf3]
[rDisp*dmin,
rForceN*f(dmin)]
[dmin,*f(dmin)]

## Slide 17
Page 17
NL Materials
Pinching4

## Slide 18
Page 18
NL Materials
Pinching4

## Slide 19
Page 19
NL Geometry
geomTransf command in OpenSees
The geometric-transformation command is used to construct a coordinate-transformation (CrdTransf) object, which transforms beam element stiffness and resisting force from the basic or natural system to the global-coordinate system. The command has at least one argument, the transformation type (Linear, PDelta, Corotational).
TIP: For the standard OpenSees beam-column elements, the difference between geometric linear and geometric nonlinear analysis lies in the geometric transformation alone, since the elements have no internal geometric nonlinearity.

## Slide 20
Page 20
NL Geometry
Coordinates in OpenSees
x’
z’
y’
x
y
z
Natural coordinates
Global coordinates

## Slide 21
Page 21
NL Geometry
geomTransf command in OpenSees
The element receives global displacements from the connected nodes
The element sends the global displacements to the geometric transformation
The element receives natural displacements from the geometric transformation
The element along with any constitutive relations (sections, etc.) compute element forces and stiffness in the natural coordinates
The element sends the element forces and stiffness in the natural coordinates to the geometric transformation
The element receives element forces and stiffness in global coordinates from the geometric transformation
The element sends (or rather makes available to send upon request) the element forces and stiffness in global coordinates to the analysis
transforms the global displacements to natural coordinates
transforms natural forces and stiffnesses to global coordinates
ELEMENT
OpenSees
Constitutive Model
geomTranf
1
7
2
3
5
6
4
Global coordinates
Natural coordinates
See Geometric nonlinearities in OpenSees

## Slide 22
Page 22
NL Geometry
geomTranf types
geomTranf
Linear
PDelta
Corotational
initial values are used for the orientation and length of the element
the transformation matrix is constant
current values are used for the orientation and length of the element
(complete “beam element”involving large displacement and rotation, but neglecting finite strains – solids!)
only second-order or “large” Delta effects
the transformation matrix is not constant

## Slide 23
Page 23
NL Geometry
geomTransf
geomTransf transfType $transfTag $vecxzX $vecxzY $vecxzZ <-jntOffset $dXi $dYi $dZi $dXj $dYj $dZj>
$transfTag | transformation tag
$vecxzX $vecxzY $vecxzZ | X, Y, and Z components of vecxz, the vector used to define the local x-z plane of the local-coordinate system. The local y-axis is defined by taking the cross product of the vecxz vector and the x-axis. These components are specified in the global-coordinate system X,Y,Z and define a vector that is in a plane parallel to the x-z plane of the local-coordinate system.
$dXi $dYi $dZi | joint offset values -- offsets specified with respect to the global coordinate system for element-end node i
$dXj $dYj $dZj | joint offset values -- offsets specified with respect to the global coordinate system for element-end node j
i
j
end offset
section offset
Not in 3D Corotational

## Slide 24
Page 24
NL Geometry
Corotational
See ex17.scd

## Slide 25
Page 25
MORE RESOURCES & REFERENCES
R&R
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Geometric nonlinearities in OpenSees
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos

## Slide 26: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick