## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
30
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28/04/21 – 05/05/21
Introduction to OpenSees
Introduction to STKO – Scientific Toolkit for OpenSees
Model definition overview
Geometry, Interactions, Selection sets, Local axes
Physical properties
Element properties
Definitions and Conditions
June-October (once a week)*
Mesh and Analysis
Analysis Command (part 1-2) - 21/07/2021
Analysis Command (part 3-4) - 28/07/2021
Postprocessing and results visualization
Modal and response spectrum analysis
Linear, nonlinear static and dynamic analysis
Reinforced concrete and masonry frame structures
(+ softening and mesh objectivity, diaphragms modelling, joints modeling, infill panels…)
*Only one in August
1
2
8
11
12
20
Full syllabus available here
THEORY
PRACTICE
INTRO
3
4
5
6
7
x2
x2
5:30 p.m.
CEST

## Slide 3
GET STARTED in OpenSees with STKO
Mesh and Analysis
8
Mesh
14 July 2021
Mesh and Analysis
8
Analysis
Controls
Seed
Build
Set-up of the analysis steps
MPCO Recorder
AnalysisCommand (defaultSettings)
Patterns
Misc_Commands

## Slide 4
Page 4
Mesh seed
Mesh
visualization
assignment: Global “Local”
all nodes of the geometry are automatically a node of the mesh
the global default seed is 1
global seed overrides Edge seed and vice-versa
remove seed works only from the selected edges/faces
assigned to the whole model
assigned only to the selection
(before clicking on Assign)

## Slide 5
Page 5
Mesh controls
Mesh
order
linear or non-linear shape function
topology
mesh unit shape for 2D or 3D elements
algorithm
structured or unstructured
Ex. Faces with ASDShellQ4 elements need to be meshed with a structured quadrilateral mesh.
compatibility: finite element – mesh topology

## Slide 6
Page 6
Mesh Build
Mesh
Building your mesh may require time and computational effort, save your model before building the mesh.
Partition your model is necessary to run your analysis with openseesmp.
(Mumps + 1 Partition)
When you modify the geometry, the mesh is lost, and so is the partition.
The mesh built is STKO is NOT and orphan mesh. You cannot select the mesh nodes and move them or edit manually the mesh configuration built by the algorithm.
always build your mesh before you hit RUN!

## Slide 7
Analysis Steps - setup
Analysis Steps
Page 7
available operations
The order in which your input your commands matters!
recorder
constraintPattern
loadPattern
AnalysesCommand
1
2
3
4
basic generic setup

## Slide 8
MPCO Recorder
recorder
Page 8
Nodal results = results at the nodes and linear along the element
Element results = results at the gauss points
except for localForce (results at the extremities of the elements, can be different at two sides of the same node)
and section.fiber.XXX (results on fibers)

## Slide 9
Add boundary conditions
load.Pattern
Page 9
The constrain.Pattern is an STKO construct, just for consistency with OpenSees nomenclature.
If they are not added here, constrains will NOT be enforced on the model

## Slide 10
Add loading conditions
load.Pattern
Page 10
The load.Pattern must contain all loads you wish to apply to the model, including prescribed displacement values.
You can create different load patterns to apply different factors.

## Slide 11
provide the solution
numbers
the dof
determines the next time step for an analysis
iterates from the last time step to the current
tests the convergence
of the solution
handles the constraints
defines the type of analysis
CTest
SolnAlgorithm
Integrator
Solver
Numberer
CHandler
Analysis
AnalysisModel
LOGIC AND ABSTRACTIONS
AnalysisCommand
Page 11

## Slide 12
Default settings
AnalysisCommand
Page 12
The default setup of the analysisCommand in STKO can be used for simply static analysis of structures directly without any modifications (if Linear you can use the Linear algorithm).
Time Step Type (Load / Displacement)
Time steps = duration/numIncr
loadConst keeps the loads constant for the next analysis stage
pseudoTime (see Week 7)
wipeAnalysis (does not destroy elements, nodes or materials, just the analysis setup)

## Slide 13
CustomCommand
Misc_Commands
Page 13
With the customCommand you can interact with your tcl script directly, as if you were programming outside of STKO.
This command guarantees that in STKO you have the full capabilities of the tcl programming language.
Ex. Common use – record command if the eigen analysis is not followed by an analysisCommand (as the record command is already invoked automatically inside the analysisCommand)

## Slide 14
monitor
Misc_Commands
Page 14
You can monitor the analysis progress directly through the monitor built-in in STKO pre-processor.
Always SAVE your plots, and when you re-run the analysis they will be erased and recreated by the command.
Specific selection sets are needed here for identifying the nodes at which to extract the desired results.
Background plot for experimental data comparisons.
Ex. Plot of the pushover curve, select the displacement results at the top and the reaction force of all the nodes at the base.

## Slide 15
rayleigh
Misc_Commands
Page 15
D = $alphaM * M + $betaK * Kcurrent +$betaKinit * Kinit + $betaKcomm * KlastCommit
Assigns damping to all previously-defined elements and nodes.
See the OpenSees documentation

## Slide 16
region
Misc_Commands
Page 16
The region command is useful to isolate part of your geometry for a specific use.
Specific selection sets are needed to ID the geometry.
Possible uses:
Add and erase geometry from the analysis
Assign rayleigh damping just to a specific geometry
Write nodes ids lists for specific result extraction.

## Slide 17
Page 17
RESOURCES & REFERENCES
R&R
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Nonlinear finite element formulations
        A tale of two element formulations
        Numerical integration options
        Massimo’s OpenSees support group
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos

## Slide 18: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick