## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
30
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28/04/21 – 05/05/21
Introduction to OpenSees
Introduction to STKO – Scientific Toolkit for OpenSees
Model definition overview
Geometry, Interactions, Selection sets, Local axes
June-October (once a week)*
Physical properties
Element properties - Next webinar 29/06/2021
Definitions and Conditions
Mesh and Analysis (2 hours on the Analysis Commands)
Postprocessing and results visualization
Modal and response spectrum analysis
Linear, nonlinear static and dynamic analysis
Reinforced concrete and masonry frame structures
(+ softening and mesh objectivity, diaphragms modelling, joints modeling, infill panels…)
*Only one in August
1
2
5
11
12
20
Full syllabus available here
THEORY
PRACTICE
INTRO
3
4

## Slide 3
GET STARTED in OpenSees with STKO
Physical
properties
4
Material
Elastic
Fiber
Aggregator
Physical
properties
Sections
Special
purpose
uniaxialMaterials
Concrete
Steel
Masonry
BeamSectionProperty
zeroLengthMaterial
truss
HingedBeam
RCJointModel3D
MasonryInfillWallMaterial
Definition (X-Objects)
Difference with other FEM
Creation and assignments
23 June 2021
Physical properties
4
3D frame structures

## Slide 4
GET STARTED in OpenSees with STKO
Physical
properties
4
Material
Elastic
Fiber
Aggregator
Physical
properties
Sections
Special
purpose
uniax.M.
Concrete
Steel
Masonry
BeamSectionProperty
zeroLengthMaterial
truss
HingedBeam
RCJointModel3D
MasonryInfillWallMaterial
23 June 2021
Physical properties
4
Differences with other FEM
STKO and OpenSees
Definition
X-Objects
Creation and assignments

## Slide 5
Page 5
Physical prop.
Definition
Physical properties mean constitutive models, everything which defines the constitutive behavior in a model.
Constitutive relationships are the heart of modelling material nonlinearities. The physical properties in STKO correspond to all material, section, and integration scheme assignments in OpenSees, all objects that provide the mathematical relationship describing the material and section behaviors.
The choice of material model depends on the structure and the finite element chosen to discretize it e(element properties).
Ex. 3D – all stress tensor components
Fiber based elements –one stress tensor longitudinal component

## Slide 6
Page 6
Physical prop.
OpenSees and STKO
construct objects
Modelbuilder
See support file: ex8.tcl, ex8.scd
create and assign physical properties
STKO
Notes: Missing last element screeshot

## Slide 7
Page 7
Physical prop.
Differences with other FEM software
no preloaded materials properties
no integration of code and regulations
complete control over constitutive models
definition of different integration schemes for each geometry and differente properties for different integration points
deeper understanding of FEM necessary
potential of programming capabilities of more than one programming language
versatile setup of the model

## Slide 8
section Elastic $secTag $E $A $Iz <$Iy $G $J>
Page 8
Physical prop.
X-Objects
all materials and sections in OpenSees correspond to Physical Property X-Objects written in Python for STKO
$secTag
$E
$G
OpenSees Commands parameters are X-Objects attributes in STKO
$Iz
$Iy
$A
$J
Each attribute has specific
metadata, of a specific type
(integer, real, string, vector etc.)
See PyMpc classes MpcXObject, MpcAttribute, MpcAttributeMetadata

## Slide 9
Page 9
Creation and assignments
Physical prop.
available operations
color coding
local axes direction modifications
Not Used
Referenced
Used
Used + Referenced
Drag on selection
Drag on selection + Ctrl
characteristic axis ≠ local axis

## Slide 10
GET STARTED in OpenSees with STKO
Physical
properties
4
Material
Elastic
Fiber
Aggregator
Physical
properties
Sections
Special
purpose
BeamSectionProperty
zeroLengthMaterial
truss
HingedBeam
RCJointModel3D
MasonryInfillWallMaterial
23 June 2021
Physical properties
4
Concrete
uniaxialMaterials
Steel
Definition (X-Objects)
Creation and assignments
Difference with other FEM software
Masonry

## Slide 11
Page 11
Materials
Uniaxial materials
See OpenSees Manual
and prof. Scott blog post on «Uniaxial Multi-Tool»
UniaxialMaterial objects in OpenSees can represent relationships in terms of:
stress-strain
Truss elements
“stress and tangent are multiplied by cross-section area to get force and stiffness”
FiberSection objects
“stress and tangent are multiplied by fiber area to get fiber force, which is summed over the section to get section stress resultants (axial force and bending moment)”
force-strain
SectionAggregator (in a beam)
“no automatic integration of the model response, stiffness
and force necessary input”
force-displacement or moment-rotation
ZeroLength elements (springs)
“no automatic integration of the model response, stiffness and force/moment
necessary input”
σ-ε
F-ε
F-d
M-r

## Slide 12
Page 12
Materials
Elastic
uniaxialMaterial Elastic $matTag $E<$eta> <$Eneg>
linear behaviour
$matTag - material object tag
$E - tangent
$eta – damping tangent (default 0.0)
$Eneg – tangent in compression (default = E)
$epscu - strain at crushing strength
See OpenSees Wiki
(it is possible to use the section Elastic command directly or the elasticBeamColumn, this can be useful to assign specific stiffness parameters, e.g. to the rigid end of an hinged beam)
N-m-s

## Slide 13
Page 13
Materials
Concrete
uniaxialMaterial Concrete01 $matTag $fc $epsco $fcu $epscu
degraded linear unloading/reloading in compression and no strength in tension
$matTag - material object tag
$fc - compressive strength
$epsco - strain at maximum strength
$fcu - crushing strength
$epscu - strain at crushing strength
N-mm-s

## Slide 14
Page 14
Materials
Concrete
uniaxialMaterial Concrete02 $matTag $fpc $epsc0 $fpcu $epsU $lambda $ft $Ets
degraded linear unloading/reloading in compression with linear softening in tension
$matTag - material object tag
$fpc - compressive strength at 28 days
$epsc0 - strain at maximum strength
$fpcu - crushing strength
$epsU - strain at crushing strength
$lambda – ratio between unloading
Slope at $epsU and initial slope
$ft – tensile strength
$Ets – tension softening stiffness
(slope of the linear tension
softening branch)
N-m-s

## Slide 15
Page 15
Materials
Steel
uniaxialMaterial Steel02 $matTag $Fy $E $b $R0 $cR1 $cR2 <$a1 $a2 $a3 $a4 $sigInit>
$matTag - material object tag
$Fy - yield strength
$E - initial elastic tangent
$b – strain-hardening ratio
parameters to control the transition
from elastic to plastic branches (recommended values)
$R0 = 10-20
$cR1 = 0.925
$cR2 = 0.15
isotropic strain hardening
N-m-s

## Slide 16
Page 16
Materials
Masonry
uniaxialMaterial Pinching4 $matTag $ePf1 $ePd1 $ePf2 $ePd2
$ePf3 $ePd3 $ePf4 $ePd4
$rDispP $rForceP $uForceP
$matTag - material object tag
“pinched” load-deformation response
degradation under cyclic loading
NA

## Slide 17
Page 17
Materials
Material Tester

## Slide 18
GET STARTED in OpenSees with STKO
Physical
properties
4
Sections
Special
purpose
BeamSectionProperty
zeroLengthMaterial
truss
HingedBeam
RCJointModel3D
MasonryInfillWallMaterial
23 June 2021
Physical properties
4
Fiber
Elastic
Aggregator
Definition (X-Objects)
Creation and assignments
Difference with other FEM software
Material
uniaxialMaterials
Concrete
Steel
Masonry
Physical
properties

## Slide 19
Page 19
Sections
Elastic (The only section that does not require a predefined material)
section Elastic $secTag $E $A $Iz $Iy $G $J <$alphaY $alphaZ>
$secTag - section object tag
$E - Young's Modulus
$A - cross-sectional area of section
$Iz – inertia moment about the local z-axis
$Iy – inertia moment about the local y-axis
$G – Shear Modulus
$J – torsional moment of inertia of section
$alphaY – shear shape factor along the local y-axis
$alphaZ– shear shape factor
along the local z-axis
One of the very few places in STKO where you find a unit system (the internal database is written in mm and the scale factor is necessary to properly represent the beam extrusion in the CAD model)

## Slide 20
Page 20
Sections
Fiber (OpenSees)
A fiber section has a general geometric configuration formed by subregions of simpler, regular shapes (e.g. quadrilateral, circular and triangular regions) called patches. In addition, layers of reinforcement bars can be specified.
There are three commands to define a fiber section in OpenSees:
section Fiber $secTag <-GJ $GJ> {
fiber $yLoc $zLoc $A $matTag
patch quad $matTag $numSubdivIJ $numSubdivJK
$yI $zI $yJ $zJ $yK $zK $yL $zL
layer straight $matTag $numFiber $areaFiber
$yStart $zStart $yEnd $zEnd }
$secTag - section object tag
$matTag – material tag associated to the fiber
$A - area of the fiber
$areaFiber – area of each fiber
($yl, $zl)
($yL, $zL)
($yK, $zK)
($yJ, $zJ)
($ystart, $zStart)
($End $zEnd)

## Slide 21
Page 21
Sections
Fiber (STKO)
In STKO there are two options to define a fiber section:

## Slide 22
Page 22
Sections
Aggregator
section Aggregator $secTag $matTag1 $dof1 $matTag2 $dof2…. <-section $sectionTag>
$secTag – section object tag
$matTag1,2,… - tag of previously-defined UniaxialMaterial objects
$dof1,2,… - the force-deformation quantity to be modeled
by this section object
$sectionTag- tag of previously-defined Section object to
which the UniaxialMaterial objects are aggregated as
additional force-deformation relationships (optional)
P Axial force-deformation
Mz Moment-curvature about section local z-axis
Vy Shear force-deformation along section local y-axis
My Moment-curvature about section local y-axis
Vz Shear force-deformation along section local z-axis
T Torsion Force-Deformation
groups previously-defined UniaxialMaterial objects into a single section force-deformation model

## Slide 23
GET STARTED in OpenSees with STKO
Physical
properties
4
Sections
Special
purpose
23 June 2021
Physical properties
4
BeamSectionProperty
Definition (X-Objects)
Creation and assignments
Difference with other FEM software
Material
Elastic
Fiber
Aggregator
Some of these do not exist in OpenSees in this form
HingedBeam
LayeredShell
RCJointModel3D
MasonryInfillWallMaterial
zeroLengthMaterial
truss
Physical
properties
uniaxialMaterials
Concrete
Steel
Masonry

## Slide 24
Page 24
Special purpose
Special Purpose
In OpenSees there is the option of assigning more than one physical property to the same element. In STKO this option is not available. The special purpose function as a container of more physical properties.
Element
1 P.P.
2 P.P.
3 P.P.
Element
1 P.P.
2 P.P.
3 P.P.
Special
purpose
1 P.P.
2 P.P.
3 P.P.
Element

## Slide 25
Page 25
Special purpose
Beam section property
You cannot directly assign an Elastic Section or a Fiber Section or a Section Aggregator to your geometry. You need to create a BeamSectionProperty.
beamSectionProperty
contains one ore more uniaxialMaterials
(depending on the chosen integration scheme)
zeroLengthMaterial
contains one ore more uniaxialMaterials
truss
contains information on the truss elements and the section object

## Slide 26
Page 26
Special purpose
Special Purpose
HingedBeam = zeroLength + BeamColumn
model concentrated plasticity approaches in 3D frame structures
RCJointModel3D = rigidLink + BeamColum
model the constitutive behaviour of RC structures joints
MasonryInfillWallMaterial = fiber + uniaxialMaterial
model the constitutive behaviour of infill panels
Automatism created in STKO to operate the assembly of existing OpenSees objects without having to code by hand in tcl, or ever draw by hand in STKO the entire assembly.

## Slide 27
Page 27
Example
Example
3D frame structure with forceBeamColumn elements loaded with with fiber sections and
See support file: ex8.tcl, ex8.scd

## Slide 28
Page 28
RESOURCES & REFERENCES
R&R
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos

## Slide 29: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick