## Slide 1
Diego Talledo
diego.talledo@iuav.it
The New ASDCoupledHinge Model for Accounting PMM Interaction within Lumped Approaches for RC Elements.

## Slide 2
Introduction
Possible modelling strategies (Deierlein et al. 2010)
Deierlein, Reinhorn, Willford. (2010). Nonlinear Structural Analysis For Seismic Design. A guide for Practicing Engineers. NIST GCR 10-917-5
Rigid-plastic hinge
Inelastic spring with hysteretic properties
Detailed finite element model
Fiber model
Hinge with finite length
Notes: Finite element modelling can be the most complex modelling strategy with discretization through the member length and cross section into finite elements. Proper constitutive laws must be defined (like for instance ASDConcrete3D)
Fiber formulation distribute inelasticity by numerical integrations through the member cross section (for obtaining the moment-curvature constitutive relation) and along the member length (permitting so the spread of inelasticity). In this case we need to define uniaxial material models in order to capture the hysteretic behaviour of the cross section and hence the member. The formulation can use displacement or force interpolation functions.

## Slide 3
Introduction
Fiber-Sections
(typically used in distributed plasticity)
Pros
  Easy to define based on geometry and 1D materials
  Automatic P-M-M coupling
Cons
  Computationally more expensive
  Cannot easily include secondary effects (bar-slip, buckling, cyclic degradation, etc..)
  Can be difficult to interpret strain demands in terms of acceptance criteria (that are more widely reported in terms of rotations)
Phenomenological Hinges
(typically used in lumped plasticity)
Pro
  Computationally more efficient
  Can include all necessary effects
  Easier to interpret results in terms of acceptance criteria
Cons
  Made of uncoupled springs (no P-M-M interaction)
  Should be calibrated for each section in your model

## Slide 4
Objective
Phenomenological Hinges
(typically used in lumped plasticity)
Pro
  Computationally more efficient
  Can include all necessary effects
  Easier to interpret results in terms of acceptance criteria
Cons
  Made of uncoupled springs (no P-M-M interaction)
  Should be calibrated for each section in your model
Develop a new Phenomenological Hinge model with P-M-M interaction
Develop a tool to easily define hinges from section geometry and materials
New ASDCoupledHinge

## Slide 5
OpenSees implementation
Idea icons created by Freepik - Flaticon
The idea:
Use uniaxial materials for individual DOFs:
N, Vy, Vz, T: elastic material (penalty stiffness)
My, Mz: Histeretic material (Pinching4)
Use a strength domain to define their interaction
Scale the material’s backbone curves step-by-step

## Slide 6
OpenSees implementation
P-M-M Strength domain
PMM strength domain provided by the user as a structured list of triplets (P, My, Mz).
The domain is internally stored in a structured mesh.
The ray of the trial internal force vector (P*,My*,Mz*), with origin of the “slice” = (P*,0,0), is intersected with the meshed domain.
Find the intersection point for the required direction.
The backbone curves of the My and Mz uniaxial materials are updated accordingly in terms of strength.
The coupling is done with the internal forces at the previous (known) time-step. No iterative coupling -> Diagonal matrix
: divisions in N (axial force) axis
: divisions in (- plane)
Cylindrical coordinate system centred in (0,0,0) and longitudinal axis aligned with P axis.

## Slide 7
OpenSees implementation
Initial stiffness, pre- and post-cap rotations
Many formulations available in literature
Give the user maximum flexibility (possibility to test different relations or define own relation)
Use of Tcl expression!
Haselton, Liel, Taylor-Lange, Deierlein (2016). Calibration of Model to Simulate Response of Reinforced Concrete Beam-Columns to Collapse, ACI Structural Journal, 113(6), 1141-1152
Initial stiffness
Cap rotation capacity
Post-cap rotation capacity

## Slide 8
OpenSees implementation
section ASDCoupledHinge3D $tag $Ktor $Kvy $Kvz $Kax
-initialFlexuralStiffness $Ky $kz
<-simpleStrengthDomain Nmin? Nmax? MyMax? MzMax? NMMax?>
<-strengthDomainByPoints $nN $nTheta {listN} {listMy} {listMz}>
<-hardening $as>
-thetaP $thetaPy $thetaPz -thetaPC $thetaPCy $thetaPCz
<-hystereticParams rDispP? rForceP? uForceP? rDispN? rForceN? uForceN?>
<-damageUnloadStiffness gk1? gk2? gk3? gk4? gklim?>
<-damageReloadStiffness gd1? gd2? gd3? gd4? gdlim?>
<-damageForce gf1? gf2? gf3? gf4? gflim?>
<-damageType type? ge?>

## Slide 9
OpenSees implementation
section ASDCoupledHinge3D $tag $Ktor $Kvy $Kvz $Kax
-initialFlexuralStiffness $Ky $kz
-thetaP $thetaPy $thetaPz -thetaPC $thetaPCy $thetaPCz
<-simpleStrengthDomain Nmin? Nmax? MyMax? MzMax? NMMax?>
<-strengthDomainByPoints $nN $nTheta {listN} {listMy} {listMz}>
<-hardening $as>
<-hystereticParams rDispP? rForceP? uForceP? rDispN? rForceN? uForceN?>
<-damageUnloadStiffness gk1? gk2? gk3? gk4? gklim?>
<-damageReloadStiffness gd1? gd2? gd3? gd4? gdlim?>
<-damageForce gf1? gf2? gf3? gf4? gflim?>
<-damageType type? ge?>
Basic parameters for the section (e.g. unique tag identifying the section, penalty stiffnesses for axial, torsion and shear DOFs)

## Slide 10
OpenSees implementation
section ASDCoupledHinge3D $tag $Ktor $Kvy $Kvz $Kax
-initialFlexuralStiffness $Ky $kz
-thetaP $thetaPy $thetaPz -thetaPC $thetaPCy $thetaPCz
<-simpleStrengthDomain Nmin? Nmax? MyMax? MzMax? NMMax?>
<-strengthDomainByPoints $nN $nTheta {listN} {listMy} {listMz}>
<-hardening $as>
<-hystereticParams rDispP? rForceP? uForceP? rDispN? rForceN? uForceN?>
<-damageUnloadStiffness gk1? gk2? gk3? gk4? gklim?>
<-damageReloadStiffness gd1? gd2? gd3? gd4? gdlim?>
<-damageForce gf1? gf2? gf3? gf4? gflim?>
<-damageType type? ge?>
Tcl Expressions for definition of initial stiffness, pre- and post-cap rotations.
Placeholders like __N__, __M__, __V__ will be replaced by the associated value of the internal forces inside the ASDCoupledHinge3D
You can even access Tcl procedures previously defined in the script!

## Slide 11
OpenSees implementation
section ASDCoupledHinge3D $tag $Ktor $Kvy $Kvz $Kax
-initialFlexuralStiffness $Ky $kz
-thetaP $thetaPy $thetaPz -thetaPC $thetaPCy $thetaPCz
<-simpleStrengthDomain Nmin? Nmax? MyMax? MzMax? NMMax?>
<-strengthDomainByPoints $nN $nTheta {listN} {listMy} {listMz}>
<-hardening $as>
<-hystereticParams rDispP? rForceP? uForceP? rDispN? rForceN? uForceN?>
<-damageUnloadStiffness gk1? gk2? gk3? gk4? gklim?>
<-damageReloadStiffness gd1? gd2? gd3? gd4? gdlim?>
<-damageForce gf1? gf2? gf3? gf4? gflim?>
<-damageType type? ge?>
Definition of PMM strength domain
Two possibilities:
Definition as structured list of triplets (strengthDomainByPoints)
Definition of a simplified domain with few data (on the safe side)

## Slide 12
OpenSees implementation
section ASDCoupledHinge3D $tag $Ktor $Kvy $Kvz $Kax
-initialFlexuralStiffness $Ky $kz
-thetaP $thetaPy $thetaPz -thetaPC $thetaPCy $thetaPCz
<-simpleStrengthDomain Nmin? Nmax? MyMax? MzMax? NMMax?>
<-strengthDomainByPoints $nN $nTheta {listN} {listMy} {listMz}>
<-hardening $as>
<-hystereticParams rDispP? rForceP? uForceP? rDispN? rForceN? uForceN?>
<-damageUnloadStiffness gk1? gk2? gk3? gk4? gklim?>
<-damageReloadStiffness gd1? gd2? gd3? gd4? gdlim?>
<-damageForce gf1? gf2? gf3? gf4? gflim?>
<-damageType type? ge?>
Definition (optional) of Hysteretic rules (Pinching4)

## Slide 13
STKO pre-processor implementation
Defined as a standard fiber section
The fiber section is only used to compute the PMM domain in STKO
Automatic tool for considering confinement effect
Tcl expression more powerful here: user can access extra variables, such as geometry (__Ag__, __W__, __H__, etc..) or material properties (__fc__, etc...)

## Slide 15
Lumped inelasticity modelling
Effective elastic stiffness:

## Slide 16
Lumped inelasticity modelling
Effective elastic stiffness:
Haselton, Liel, Taylor-Lange, Deierlein (2016). Calibration of Model to Simulate Response of Reinforced Concrete Beam-Columns to Collapse, ACI Structural Journal, 113(6), 1141-1152

## Slide 17
Lumped inelasticity modelling
Effective elastic stiffness:
System in series:
Stiffness of elastic element:
Total system stiffness (e.g. Haselton et al. 2016)
Spring element (zerolength section):

## Slide 18
Lumped inelasticity modelling
System in series:
Stiffness of elastic element:
Total system stiffness (e.g. Haselton et al. 2016)
Spring element (zerolength section):
Effective elastic stiffness:
Rotational stiffness for our constitutive law:

## Slide 19
Conclusion & Future developments
Conclusions:
ASDCoupledHinge A new phenomenological hinge section is proposed
PMM interaction is accounted for both for Moments and Rotations
Use of Tcl Expressions to give the user maximum flexibility in implementing its own hinge properties
Future Developments:
PR submission to OpenSees & OpenSees documentation repos
Improve the GUI permitting an easier management of the different expressions for the hinge properties (work in progress)
Extend also to Python interpreter (work in progress)
Extend to PMMVV interaction (shear – flexure interaction)
Allow users to define Tcl Expression for the other DOFs (Vy and Vz for example)

## Slide 20
Diego Talledo
diego.talledo@iuav.it
The New ASDCoupledHinge Model for Accounting PMM Interaction within Lumped Approaches for RC Elements.
THANK YOU FOR YOUR ATTENTION!

## Slide 26
Elastic element
Total response
Elastic
Inelastic
Elastic element

## Slide 27
Elastic element (uncracked)