## Slide 1: GET STARTED in OpenSees with STKO
starting from scratch
20 classes
Welcome to:
Support materials uploaded here within 24h
30
min
??
Image courtesy of ESO

## Slide 2
CONTENTS
GET STARTED
in OpenSees with STKO
28/04/21 – 27/10/2021
Introduction to OpenSees
Introduction to STKO – Scientific Toolkit for OS
Model definition overview
Geometry, Interactions, Selection sets, Local axes
Physical properties
Element properties
Definitions and Conditions
Mesh and Analysis
Analyses Command (part 1-2)
Analyses Command (part 3-4)
Postprocessing and results visualization
Linear elastic analysis
Material and geometrical nonlinearities
Modelling approaches to plasticity
Nonlinear static (pushover) analysis
Nonlinear time history analysis
Modal and response spectrum analysis
Reinforced concrete, steel and masonry frame structures
(diaphragms modelling, joints modeling, infill panels…)
17
20
Full syllabus available here
THEORY
PRACTICE
INTRO
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16

## Slide 3
GET STARTED in OpenSees with STKO
Modal and response spectrum analysis
Modal and response spectrum
Common errors
Results post-processing
06 October 2021
Modal and response spectrum analysis
Response Spectrum analysis in STKO
17
17
Modal analysis in STKO
Eigen command in OpenSees
Eigenvalue analysis in STKO

## Slide 4
Page 4
Week 17
See ex27.scd
EdgeMass
FaceMasses
3D frame structure with rigid diaphragms
Example

## Slide 5
Page 5
eigen in OS
eigenCommand
Compute just eigenvalues (lambdas) without providing any derived quantities useful in modal analysis.
eigen <$solver> $numEigenvalues
Default setup:
-generalized
(modal analysis is a generalized analysis)
-findLargest False
(we are interested in lowest eigenvalues which give us the highest periods)
-genBandArpack solver (functions with sparse matrices for large models, limited to N-1 number of eigenvalues)
You do not choose the normalization method, the solver does!

## Slide 6
Page 6
eigen in OS
eigenCommand
3 options:
-generalized (frequency) or –standard (to find eigenvalues of a matrix – not used)
-findLargest (to find the highest periods – buckling?)
-solver:
-genBandArpack (default and suggested!)
(it searches just for the eigenvalues that you are requesting, and it works with sparse matrices, a mass-normalization is operated on the eigenvalues which means the effective modal mass is the identity – limitation: if you try to extract more eigenvalues > NDOF with an associated mass it will fail)
-symmetricBandLapack
(actually, diagonal matrix is required, for standard problems - for nodal masses is fine but if you use consistent mass matrices, for example with the displacement beam column or with solid elements it will fail)
-fullGenLapack
(it searches for all the possible eigenvalues, and works with dense matrices, a displacement-normalization is operated based on the maximum displacement or rotation depending on the kind of mass applied - if your model is small it will work, with a large model you will run out of memory!)

## Slide 7
Page 7
eigen in STKO
Eigen analysis in STKO
gravity or dummy analysis before
(otherwise default analysis setup!)
record command after
(otherwise modesOfVibration will not be saved in the mpco database)

## Slide 8
Page 8
Common errors
Common errors in eigenvalue analysis in OpenSees with STKO
“Starting vector is 0” – There are no dynamic dofs in your model, did you input mass??
“Eigenvalues were never set” – Are you asking too many eigenvalues with genBandArpack solver?
Weird results! – Are you assign the eigen command without a setup analysis before?
Still weird results!!! – Are you using wipe in your setup analysis?
Other - Are you trying to run the eigen command on parallel processes? YOU CAN’T!
I can’t see the eigenvector results!! – Did you put the record command in a customCommand after your eigen analysis?
My periods are too high!! – Check your units!
Argument not in valid range – You may have negative eigenvalues, maybe
your model is not well constrained, check your boundary conditions.

## Slide 9
Page 9
modalProperties
modalProperties Command
Modal results for each mode
No mandatory parameters
-print
(prints modal properties in the command window, without printing they will be available for response spectrum analysis, but they won’t be accessible)
-file
(prints modal properties on an external file)
-reportFileName
(name of the file - the file will be inside the folder in which you are running OpenSees, unless you specify a relative path)
-unorm
(displacement-normalized version of the eigenvectors – only modal participation factors are influences by normalization, not the participation masses)
modalProperties <-print> <-file $reportFileName> <-unorm>

## Slide 10
Page 10
modalProperties
modalProperties Command
Generalized mass
Modal Participation Factors
for a certain mode, it indicates how strongly motion in the global x-, y- or z-direction or rotation about one of these axes is represented in the eigenvector of that mode.
defines the magnitude of the rigid body response of a degree of freedom to imposed rigid body motion (displacement or infinitesimal rotation) in the i-direction
Modal participation masses
coupling between translational and rotational masses

## Slide 11
Page 11
modalProperties
modalProperties Command
Domain size
Eigenvalue analysis
(eigenvalues)
Total mass of the structure
(rotational mass are the direction rotational + the translational times the distance to the center of mass, including masses of constrained nodes if present)
Total free mass of the structure
Center of mass of free masses
(coordinates of the center of mass)
Modal participation factor
(the participation factor for a certain mode 'a' in a certain direction 'i’ indicates how strongly displacement along (or rotation about) the global axes is represented in the eigenvector of that mode)
Modal participation masses for each node (absolute)
Modal participation cumulative mass for each node (absolute)
Modal participation mass ratios for each node (%)
Modal participation cumulative mass ratios for each mode (%)

## Slide 12
Page 12
responseSpectrum
responseSpectrum Command
responseSpectrum $tsTag $direction <-scale $scale> <-mode $mode>
tsTag
(timeSeries path with the responseSpectrum to be studied)
direction
(direction of the response spectrum analysis)
-mode (optional)
(extract results only at the specified mode)

## Slide 13
Page 13
Post-processing
Results post-processing – Modal combination
See utils_18.py
as many steps as many modes in the eigenvalue analysis

## Slide 14
Page 14
Post-processing
Results post-processing – Modal combination
See utils_18.py

## Slide 15
Page 15
MORE RESOURCES & REFERENCES
R&R
Installation guide
Python documentation
PyMpc Documentation
MPCO Documentation
OpenSees Validation
HDF group
HDF viewer
Michael Scott’s blog index
Geometric nonlinearities in OpenSees
Modal and Response Spectrum Analysis from Dr. Petracca (webinar #17)
Official webpage
OpenSees Wiki
OpenSees Manual
GitHub documentation
OpenSees Wiki
OpenSees Community
OpenSees Facebook
OpenSees source code
Basic OpenSees Examples
OpenSees support group on youtube
(to get in send an email to pchi893@aucklanduni.ac.nz)
Silvia Mazzoni’s site
Michael Scott blog
STKO purchase page
NAFEMS
STKO Manual
Tutorial videos

## Slide 16: Thank you for your attention!
Following:
Q/A Session
Dive into the forum!
Graphics credits:
Slidecarnival
Freepick